## Slide 1
JOB ROLE – HAND EMBROIDERER
ADDAWALA
Sector – Apparel, Made-Ups and Home Furnishing
(Qualification Pack Code: AMH/Q 1001)
Class X
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in

## Slide 2
UNIT 4: APPLICATION OF EMBROIDERY STITCHES
Session 3: Specification Sheet

## Slide 3
Content
Title | Slide No.
Session Objectives | 4
Specification sheet | 5
Instructions given in an embroidery spec sheet | 9
Summary | 11

## Slide 4
Session Objectives
The students will be able to:
Explain and interpret buyer’s specification sheet given for embroidery work.

## Slide 5: SPECIFICATION SHEET
It is a document that includes garment sketch and garment construction details.
Specification sheet is also known as spec sheet or simply garment spec.
This sheet is made to explain design details and methods of construction.

## Slide 6: Things included in a spec sheet
Product sketch: The design of the end product is showcased using a flat sketch/technical sketch with details marked on it.
Fabric details: Swatches of the fabric with color details or the fiber content is mentioned.
PoMs (Points of Measure): Size measurements of the required item, which assures the measurement of the final product. This is very important as it ensures the accurate execution of the garment during its production.

## Slide 7
Design placement: Details of the design and its placement or repeat, design arrangement is defined for the exact placement on the actual sample.
Embroidery placement: Information regarding the size of motif, its placement, type of stitches, tools and raw material for embroidery and colour combination of material used are also clearly mentioned.
Workmanship Instructions: Particulars of stitch type, seam diagram, thread size and SPI (stitch per inch) are also mentioned.

## Slide 8
Garment washing instructions: Specific instructions for washing and finishing for embroidered product is also mentioned.
Accessories details: Details of trims, fasteners etc. required with product codes are given.
Label placement: Placement details are given for brand logo labels and care labels in the garment.
Comment section: comment section provides notes of small details to be followed during construction and finishing.

## Slide 9: Instructions given in an embroidery spec sheet
Type of embroidery thread
The base fabric for embroidery work
Type of other decorative materials along with embroidery
Placement of embroidery design on the fabric or product
Size of embroidery design
Colours of embroidery thread
Placement of different beads, sequins, stone etc.
Stitch density
Estimated stitch length
Type of stitches

## Slide 10: Example of an spec sheet

## Slide 11
Summary
19
In this session, you have learnt about use and proper interpretation of buyer’s specification sheet given for embroidery work.

## Slide 12
18
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Project Coordinator : Prof. Pinki Khanna
Academic Support – Nupur Srivastava & Shivangi Vig
Assistance Graphic Artist
Vani Pandya Prachi Verma