## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 5: CONSTRUCTION OF GARMENTS FOR CHILDREN AND FEMALES
Session 2: Pattern Markings And Layout

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Fabric marking | 6
Fabric layout | 10
Special layout | 19
Summary | 22

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about fabric placing, marking and cutting.

## Slide 5: PATTERN MARKINGS & LAYOUT
A layout is a plan for the placement of pattern pieces on the fabric to use the maximum space in the fabric and avoid wastage.

## Slide 6: Fabric markings
Grain line: It is the direction of yarns in the fabric.
The grainline parallel to the warp yarns is called lengthwise grain. Whereas the grainline parallel to the weft yarns is called crosswise grain.
The grainline defines the orientation of yarns in a fabric.

## Slide 7
Cutting Lines: It indicates where to cut the fabric to match the shapes on the pattern. They are solid lines and easy to identify.
Pattern Adjustment Lines: These lines allow you to make a garment longer or shorter based on your needs. These run across a piece and usually appear as two parallel lines. The space between the lines depends on the degree of lengthening or shortening required.

## Slide 8
Fold Lines: When cutting a symmetrical piece, patterns often recommend folding the fabric in half. When unfolded, the fabric forms the desired shape, takes less cutting time, and guarantees perfect symmetry.
Stitch Lines: These are the markings that convey the where to stitch the fabric pieces. Stitch lines are symbolized as dotted line in a pattern.

## Slide 9
Notches: Diamond or trapezoidal shaped symbols along the seam line are used both in pattern layout and during construction.

## Slide 10: 2. Fabric layout
The amount of fabric is calculated according to the length of garment.
Generally, it is double the length plus sleeve length plus five to ten inches extra (for belts, collars, pockets etc.)
For example, if the length of the kurta is 40” and the sleeve length is 10” than the total fabric required is 40” +40” =80” +10” +10” extra =100” or 2.5 meter.

## Slide 11: Points to be remembered in pattern layout
Press the fabric as well as the pattern pieces flat before laying the pattern on the fabric.
Use a large table or any hard flat surface for accommodating the work.
If an open layout is used, place the fabric right side up on the table. For all other layouts, fold the fabric right sides facing and wrong sides out.
The best way to cut a fabric is to keep it on fold. The fold of fabric depends on the width of fabric, type of cloth, width of pattern pieces and design of garment.

## Slide 12
Before fabric cutting one must keep the pattern pieces and pin them for a trial.
One must remember to leave seam allowances while cutting. There must be enough fabric to cut belts, facing, pockets, etc. for which paper patterns are not prepared.
Fold lines on the patterns must be kept on folded edges of fabric.
Pin patterns to the fabric firmly.
Use special layouts for asymmetric designs and for fabrics with designs such as stripes and checks, designs going in one direction and fabrics with nap and pile.

## Slide 13: Methods of pattern layout
Lengthwise center fold: Here the fabric is folded down the middle parallel to the selvedges so that the selvedges come together. This layout is common for most of the garments.

## Slide 14
Off center lengthwise fold: This is used when narrow pieces have to be cut on fold.
Here the fabric is folded down the middle parallel to the selvedge.

## Slide 15
Crosswise centre fold: This is suitable for materials that are too narrow to accommodate the width of pattern pieces when folded lengthwise.
Here the fabric is folded down the middle perpendicular to the selvedge or crosswise.

## Slide 16
Off center crosswise fold: When only a part of the material is required to cut pattern pieces that are too wide for lengthwise fold layout, this type of fold is used.
Here the fabric is folded down perpendicular to the selvedge or crosswise as required.

## Slide 17
Double fold: It is used when many pattern pieces that are not too wide must be cut on fold.
Here the fabric is folded in such a way that the selvedges meet at the center for e.g., kurta and tops.

## Slide 18
Combination fold: Here, lengthwise fold and crosswise fold are combined.
Open layout: In this type of layout, the fabric is not folded at all. This is used especially for designs, which require right and left halves to be cut separately.

## Slide 19
3. Special Layouts
Fabrics with lengthwise striped design: While cutting fabric with bold stripes, adjust the position of the pattern so that one of the prominent lines falls along the center back of the garment and the remaining strips are identical on the two sides of the fold.

## Slide 20
Fabrics with bold designs such as plaids, and crosswise stripes: Match plaids and stripes so that they form continuous lines across seam openings or meet at equal angles. When you fold such fabrics to keep the pattern pieces, make sure that the stripes are matching exactly on both layers of fabric.

## Slide 21
Fabrics with one-way design: When cutting these fabrics, one must take care to see that all the pattern pieces are arranged in the same correct direction. The print will look upside down on sections, which have been placed wrongly.

## Slide 22: Summary
In this session you have learnt about fabric placing, marking and cutting.

## Slide 23: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma