## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 6: CARE AND MAINTENANCE OF SEWING MACHINE
Session 2: Machine And Sewing Defects And Its Solutions

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Sewing machine defects and its solutions | 5
Sewing defects and its solutions | 15
Summary | 24

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge fabric selection and types of fabric used for garment construction.

## Slide 5: SEWING MACHINE DEFECTS AND ITS SOLUTIONS
Defects can be defined as the faults or imperfections that one may encounter while working.
Sewing defects refer to the faults or imperfections during sewing that affects the overall look and quality of a garment.

## Slide 6: Defect: The machine does not feed the material
POSSIBLE CAUSES | CORRECTIVE ACTION
The stitch length has been set to zero. | Set the proper stitch length.
The presser foot pressure is too low. | Set pressure of presser foot.
Feed dog is lowered. | Raise feed dog.
Threads are knotted under the fabric. | Remove fabric and knotted threads. Then again place the fabric properly.
 | Place both threads back under the presser foot before starting to sew.

## Slide 7: Defect: Machine running heavily
POSSIBLE CAUSES | CORRECTIVE ACTION
Dust or lint clogging under the feed dog. | Clean the feed dog.
Insufficient oiling | Oil the machine properly.
Thread caught in the shuttle | Remove the thread from the shuttle.
Machine not used for some time with the result that the parts have jammed | Disassemble the removable parts, clean and oil them.

## Slide 8: Defect: The sewing machine does not run.
POSSIBLE CAUSES | CORRECTIVE ACTION
The presser foot is not properly placed and the needle hits the presser foot. | Place and tighten the presser foot properly.
The needle has come out and is in the shuttle area of the machine. | Remove the needle and insert a new one again, or place it at the right position.

## Slide 9: Defect: The upper thread breaks.
POSSIBLE CAUSES | CORRECTIVE ACTION
The threading is not correct. | Thread the machine correctly.
The thread has a knot in it. | Remove knots from the thread.
The upper thread tension is too tight/high. | Make correct the thread tension.
The needle is bent or blunt. | Replace with a new needle.
Wrong size of needle | Replace with a needle of the correct size.
The needle has been inserted wrongly. | Insert the needle properly.
The needle and thread do not match. | Use a suitable thread and needle.
Started stitching too fast | Start the machine at a medium speed
Thread take-up lever has not been threaded | Check the threading order.

## Slide 10: Defect: The bobbin thread breaks
POSSIBLE CAUSES | CORRECTIVE ACTION
The bobbin has not been fully inserted/pushed in the bobbin case. | Securely install the bobbin in the bobbin case.
The bobbin does not turn smoothly in the bobbin case. | Thread the bobbin case correctly.
Lint in the bobbin case or shuttle | The bobbin should not be overwound.
The bobbin does not turn smoothly in the bobbin case. | Check that the bobbin has been wound evenly.
 | Clean the bobbin case and shuttle, and remove the lint.

## Slide 11: Defect: Loud noise is heard and/or knocking noise; machine jammed
POSSIBLE CAUSES | CORRECTIVE ACTION
Dust has accumulated in the feed dog. | Clean the machine and remove the lint.
Lint is in the hook and shuttle area. | Disassemble the shuttle case and clean it.
The thread is caught in the shuttle | Oil the machine.

## Slide 12: Defect: Threading cannot be done
POSSIBLE CAUSES | CORRECTIVE ACTION
The needle is not at the highest position. | Turn the hand wheel until the needle reaches its highest position.

## Slide 13: Defect: The thread does not enter the eye of the needle.
POSSIBLE CAUSES | CORRECTIVE ACTION
The eye of the needle is clogged. | Clogging should be removed by using a fine wire.
The thread is thick in comparison to the eye of the needle. | Change the needle.
 | Select the thread according to the needle.

## Slide 14: Defect: Needle breaks
POSSIBLE CAUSES | CORRECTIVE ACTION
A thin needle was used for sewing a heavy weight material. | Use the correct size of the needle.
The needle has not been fully inserted/pushed into the needle bar. | Properly insert/push the needle in the needle bar.
The screw of the needle clamp is loose. | Use correct presser foot.
The presser foot is not the correct one. | Reset the presser foot.
The presser foot is loose. | Do not pull fabric; guide it gently.
Pulling of fabric | 

## Slide 15: SEWING DEFECTS AND ITS SOLUTIONS
Faulty stitching can affect the overall look of the final garment and hence can degrade the quality.
Early identification and rectification of such defects is important to save time and money.

## Slide 16: Defect: Skipped stitches
POSSIBLE CAUSES | CORRECTIVE ACTION
The thread tension is too tight/high. | Correct the thread tension.
The needle is bent or blunt. | Replace with a new needle of good condition.
Wrong size of the needle | Replace with a needle of correct size.
The needle and thread do not match. | Use a suitable thread and needle.
The thread take-up lever has not been threaded. | Check the threading order.
Light pressure on the presser foot | Increase pressure on the presser foot.
Incorrect setting of the needle | Reset the needle properly.

## Slide 17: Defect: The stitches are not formed properly
POSSIBLE CAUSES | CORRECTIVE ACTION
The thread has not been pulled into the thread guide. | Fully pull the thread into the thread guide
Threading is not correct. | Correct the threading.
The bobbin case has been threaded wrongly. | Correctly thread the bobbin case.

## Slide 18: Defect: Irregular stitches
POSSIBLE CAUSES | CORRECTIVE ACTION
Incorrect size of the needle | Choose the correct size of the needle for the thread and fabrics.
Improper threading | Rethread the machine properly.
Loose upper thread tension | Tighten the upper thread tension.
Pulling of the fabric | Do not pull the fabric; guide it gently.
Light pressure on the presser foot | Increase pressure on the presser foot.
Loose presser foot | Reset the presser foot.
Uneven or overwound bobbin | Rewind the bobbin properly.

## Slide 19: Defect: Fabric pucker
POSSIBLE CAUSES | CORRECTIVE ACTION
The stitch length is too long for the material. | Decrease the stitch length.
The needle point is blunt. | Replace with a needle of good condition.
Incorrect thread tension. | Reset the thread tension.
Light pressure on the presser foot. | Increase pressure on the presser foot.
The fabric is too sheer or soft. | Use an underlay of tissue paper/backing.
Using two different sizes or kinds of upper and lower threads | The upper thread and bobbin thread should be of the same size and kind.

## Slide 20: Defect: Bunching of thread
POSSIBLE CAUSES | CORRECTIVE ACTION
The upper and lower threads are not drawn back under the presser foot. | Draw both threads back under the presser foot.
The placement of the feed dog is down. | Fit the feed dog properly.

## Slide 21: Defect: Seam Slippage
POSSIBLE CAUSES | CORRECTIVE ACTION
This defect occurs when yarns of the fabric are pulled out of the seam. | Stitch density should be optimized.
 | Use French seam in place of plain seam.
 | Increase the width of seam

## Slide 22: Defect: Unbalance stitch
POSSIBLE CAUSES | CORRECTIVE ACTION
The thread tension is incorrect. | Set accurate thread tension.
Threading is not correct or incorrect thread path. | Correct the threading of both bobbin and needle thread.
Snagging of needle with bobbin case. | Bobbin case must be smooth.

## Slide 23: Defect: Seam grin
POSSIBLE CAUSES | CORRECTIVE ACTION
When the two panels of fabric are open, a gap is revealed. | Increase stitch tension.
Lower stitch tension. | Increase stitches per inch (SPI).
Incorrect stitches per inch (SPI). | 

## Slide 24: Summary
In this session you have learnt about fabric selection and types of fabric used for garment construction.

## Slide 25: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma