## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 1: INTRODUCTION TO CLOTHING, TAILORING AND SEWING MACHINE
Session 2: Terminology Related To Sewing And Garments

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Terminologies | 5
Summary | 65

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about terminologies related to garment.

## Slide 5: TERMINOLOGY RELATED TO SEWING AND GARMENTS
A
Alter: It refers to changing or revising a pattern or garment to suit individual sizing or comfort.
Anchoring stitches: These are back stitches at the seam edges in order to prevent the ripping off or pulling out of the seam.
Appliqué: A surface embellishment that employs small patches or fabric pieces which are sewn on a larger fabric or surface.

## Slide 6
Apex: The highest point on the bust for ladies’ garment.
Armhole: It is a hole for the arm where bodice joins the sleeve.
Armscye: It is used to describe the scooped-out curve of the armhole on a block or pattern.

## Slide 7
B
Balance: It refers to the hang and proportion of the garment.
Balance point: It is a mark made on the various pieces of the garment to maintain a balance while stitching.
Baste: To stitch the pieces of a fabric together temporarily using long running stitches created by hand or by machine.

## Slide 8
Basting: Basting refers to temporarily joining pieces of fabric before stitching them firmly.
Bell sleeve: A style of sleeve that is full and flared at the elbow or wrist level.
Bias: It is a diagonal line across the grain of the fabric.
Bias binding: Also called bias tape, a bias-cut strip used to bind or cover edges of necklines and armholes.

## Slide 9
Bias cut: Any diagonal cut that is not on the lengthwise or crosswise grain is a bias cut.
Bias facing: A bias-cut fabric strip which is used for finishing neckline, armholes.
Binding: It is a strip of fabric used to cover a seam edge or to enclose raw edges. It can be straight or bias.
Blanket stitch: It is a stitch that is used to reinforce and finish the edges of blanket or other thick material.

## Slide 10
Blending: It means to mix different type of fibers.
Blind hemming (stitch): It is a hemming (stitch) that is not visible on the face of a fabric or garment
Bobbin winder tension angle: It is a device situated near the bobbin winder which helps to wind the bobbin evenly.
Bodice: The front and back upper part of a pattern or garment that runs from shoulder to waist.

## Slide 11
Bodkin: Long, flat, needle-like tool used to thread elastic through a loop
Brocade: It is a woven textile having a raised floral or figured design that is introduced during the weaving process.
Buckram: A heavy, coarse stiff cotton fabric used for interfacing and stiffening parts of garments such as collars, cuff and hats.
Button: It is a fastener which is used to close an opening in the garments or any other article., material and colours.

## Slide 12
Cambric: It is a soft, plain weave cotton or linen fabric which is closely woven, usually with slight stiffening.
Canvas: It is a general classification of strong, firm, closely woven fabrics usually made with cotton, originally made of hemp.
Carding: It is a mechanical process that disentangles, cleans and intermixes fibers to produce a continuous web or sliver suitable for subsequent processing.
C

## Slide 13
Casing: Folded and stitched tunnel of fabric that holds elastic, cording, or boning.
Centre point: The point that is equally distant from every point on the circumference of a circle or sphere or place in the middle.
Chain stitch: It is a stitch formed by making connected loops that form a chain.
Chiffon: It is a very lightweight, sheer silk or man-made fabric made in a plain weave with fine, spun yarn.

## Slide 14
Clip: It is a small snip or cut made in the edge of fabric.
Combing: It is a technique whereby fibers are passed through a series of straight, metal teeth in order to lay the fibers parallel to one another.
Corduroy: It is a strong durable fabric with a rounded cord, rib, or wale surface formed by cut pile yarn.

## Slide 15
Couching: A method of embroidering in which a design is made by various threads/ cords and secured by fine stitches drawn through the material and across the cord.
Crêpe: It is a general classification of fabric that may be made of silk, rayon, acetate, cotton, wool, man-made fibers, or crinkled or grained surface effects.
Cross grain: It refers to the direction of weft yarns which is perpendicular to warp yarns and selvedge of fabric.

## Slide 16
Crotch Depth: It is the measurement from waist to bottom of the crotch.
Crotch Length: It is the measurement from front waist through the legs to back waist.
Crotch point: This is where the inside leg seams meet the crotch seams in a trouser.
Cutting board: A specially constructed, folded, corrugated board which opens out to cover a table or bed.
Cutting Line: On a pattern, the outermost solid dark line is the line upon which the pattern is cut.

## Slide 17
Dart: It is a wedge or diamond-shaped section which is used to shape a flat piece of fabric to fit the curves of a figure.
Dart intake: It is the amount of fullness that is controlled by a dart in order to shape the fabric.
Dart Point: The tip and pointed end of a dart.
Denim: A well-known basic cotton or blended fabric usually woven in a 2/1 or 3/1 warp- faced right hand twill weave.
D

## Slide 18
Dobby weave: A style of patterned surface figure weave consisting of small repeating geometric designs.
Double-fold hem: It is a hem that is folded once for the hem allowance and a second time to enclose the raw edge.
Double needle: A machine needle attached to a single shaft that sews two parallel rows of stitches at once
Drafting: It is a step/system for pattern making that depends on the measurements taken from a dress form or model.
Draping: It is the process of positioning and pinning fabric on a dress form to develop the structure of a garment design.

## Slide 19
Ease: It is the amount of space added to the measurements in order to ensure ease for movement.
Easing: This is needed when joining two edges that are of different lengths and shape.
Edge stitch: It is a kind of straight stitching very close to the edge of a seam, trim, or outer edge to secures seam allowances, prevents the edge from stretching, and supports the fabric.
E

## Slide 20
Eye: It is the part on the needle that carries the thread to: keep forming stitches.
Eyelets: It is a small hole, usually round and finished along the edge, as in cloth or leather for the passage of a lace or cord.

## Slide 21
Fabric weight: It depends on the thickness of the threads, the density of the weave or knit, & its composition.
Fabric width: It is the fabric length from one selvedge edge to the other selvedge or the length of fabric along the weft yarns.
Facing: It is an extra layer of fabric stitched on the inner side of a garment for strength and edge finishes.
F

## Slide 22
Feeding devices: These are the parts of a sewing machine which are used to advance and raise the fabric while stitching.
Felt: It is a non-woven sheet of matted material made from wool, hair, fur, or certain manufactured fibers.
Filament: It is a fiber of indefinite or extreme length.
Flare: It is a shaped fullness added to the different parts of a garment.

## Slide 23
Floss: It is a soft thread of silk or mercerized cotton used to clean tension discs, feed dog, etc..
Flounce: It is a full circular edging for the neckline, sleeves and hems.
Forearm seam: It is the seam nearest to the front of a two-piece sleeve.
Fray: The wearing out of the fabric at the edge due to friction or constant rubbing
French curve: A drafting tool that enables one to draw smooth curves for e.g., armholes.

## Slide 24
Frill: It is a strip of fabric of any width gathered and attached to a garment as an edging.
Fringe: It is a decorative edge made of hanging strings of thread or fabric.
Fullness: It is an extension on one of two sections of a garment joined by a seam, used to create volume or shape in the garment.

## Slide 25
Fusible: It is a type of fabric or material that has heat-sensitive adhesive on one side that enables it to bind to another fabric.
Fusible interfacing tape: On heating, this tape fuses to fabric to stabilize a seam or edge.
Fuzz: It refers to the fiber ends that protrude from a yarn or fabric.

## Slide 26
Gathers: Gathers are graceful folds of fabric that provide fullness, suggesting a soft look, which can be made using machine or hand stitches.
Gathering: A method of distributing fullness over a given area
Gore: Vertical garment sections, usually on a skirt.
G

## Slide 27
Grain: It is the direction of yarns in a woven fabric along the length to across the width.
Grain line: It is a line drawn from end to end on the pattern piece to show how the pattern should align with the lengthwise grain of the fabric.
Grading: It is a method of proportionately increasing or decreasing the size of an original pattern.
Gusset: It is a small piece of fabric inserted in the seam to allow room for movement.

## Slide 28
Halter: It is a style of neckline that has a strap or an extension of fabric running from the front armhole to the back of the neck
Ham : It is a tightly stuffed small pillow used as a curved mold when pressing curved areas.
Hand overcast: A hand stitch that wraps around an edge like a spiral.
Hand: The way a fabric feels in the hand, e.g., smooth, soft, rough and crisp.
H

## Slide 29
Handle: it is attached to the handle attachment of the machine and helps to drive it with hand.
Hem: It is an edge finish used to finish the bottom edge of a garment or any other article.
Hem allowance: It is the distance between the cutting line and the hemline
Hemline: It is the lowest edge of the garment once the hem is sewn.

## Slide 30
Hemp: It is a fine, light coloured, lustrous, and strong bast fiber, obtained from the hemp plant.
Hip curve: A curved ruler used to give shaping on the pattern at hip area.
Hook: A piece of metal or other hard material curved or bent back at an angle, for catching hold of or hanging.
Hoop: A plastic, metal, or wooden frame that holds fabric tight while sewing or embroidering.

## Slide 31
Interfacing: It refers to a sew-in or fusible fabric used to stabilize the fashion fabrics.
Interlacing: During stitching, when one thread passes over or around another thread or loop of another thread, it is called interlacing.
Inter-looping: It is the passing of a loop of thread through another loop formed by a different thread.
I

## Slide 32
Intra-looping: When a loop of one thread passes through the loop of the same thread during sewing
Invisible zippers: An invisible zipper is a concealed zipper which is hidden within the seam.

## Slide 33
Jacquard weave: A decorative designs involves at least two basic weaves in various arrangements to form the pattern.
J

## Slide 34
Lapel: Lapel is folded flap of jacket, coat etc., turned back which usually becomes an extension of collars in garments
Loop stitches: These are stitches formed by the loop section of a serge or over locker.
Lining: A fabric (usually lightweight) which helps to cover the stitching details on the inside of the garment.
Linen: This fiber is obtained from the stem of the flax plant. Linen is a strong and durable fabric.
L

## Slide 35
Marker Making: Marker making is the process of determining a most efficient layout of pattern pieces to minimize fabric wastage during cutting.
Mending: It is a finishing process in fabric manufacture in which irregularities such as weaving imperfections, tears, and broken yarns are repaired after the cloth is taken from the loom.
Marking chalk: These are made of colored powder that is used to transfer markings on to the fabric.
M

## Slide 36
Mercerized thread: It is a boil-fast, plied, corded cotton thread which has been treated with caustic soda, to give it more strength, luster and affinity for dyes.
Mercerizing: It is a treatment of cotton yarn or fabric with strong alkali to causes a permanent swelling of the fiber.
Multi size pattern: A commercial pattern printed with several sizes on each pattern piece.

## Slide 37
Muslin: It is basically an unbleached plain woven cotton fabric used for making test fits.

## Slide 38
Nap: It is a layer of fiber ends raised from the ground weave of the fabric by a mechanical brushing action.
Notch: It is a small cut that is shaped like a ‘V’ and that is made on an edge or a surface.
Needle clamp: It is a screw that is tightened to hold the needle in position.
N

## Slide 39
Organza: It is a light weight, transparent fabric in plain weave with a crisp hand that usually is made of very fine filament yarns.
Overcast stitch: It is a slanting stitch used around cut edges or open parts to prevent raveling.
O

## Slide 40
Pattern Blocks: A block pattern is a custom-fitted, basic pattern which can be altered to create designs for many different styles it is also called as sloper.
Pattern: It is the paper or cardboard template from which the parts of a garment are traced onto the fabric before cutting out and assembling.
Pattern drafting: Drawing a paper pattern by positioning lines, points, and curves in a prescribed manner based on body measurement.
P

## Slide 41
Pile: A surface effect on a fabric formed by upright yarns, cut or loops of yarn raised from the surface of the fabric
Pinning: Attaching pins for keeping fabric and pattern in place.
Piping: A narrow piece of bias-cut fabric folded over a cord/without cord and stitched into the seam with the raw edge of a garment.
Placket: It finished opening of a garment that enables easy slip on and off on the body.

## Slide 42
Plain weave: A weave in which each weft yarn passes alternately over and under each warp yarn in a square pattern.
Pleat: It is a type of fold formed by doubling the fabric back up on itself and securing it in place.
Ply: It is one of the strands in a yarn. The thickness of yarn is also determined by how many plies or strands it has twisted together.

## Slide 43
Point presser: A small tool used to insert into a tight corner or small space for ease of pressing
Polyester fabric: It is a generalized term for any fabric, which is made using polyester yarns or fibers.
Point turner: A tool used to turn a sewn corner to the right side with a sharp, crisp point
Pre-shrink: Washing the fabric before cutting to allow it to shrink depending upon the type of fabric

## Slide 44
Princess seam: It is a lengthwise seam passing through the apex and giving shape to the garment.
Pucker: It is tightly gathered or contracted wrinkles or small folds, caused due to incorrect density of stitches, blunt point needle, insufficient backing, and incorrect thread tensions

## Slide 45
Raw edge: Fabric ends with an unfinished look
Rib weave: It is a variation of plain weave with visible stripes in either warp direction or weft direction.
Ripping: To cut or tear apart in a rough or vigorous manner to rip open a seam
R

## Slide 46
Right side of the fabric: For a solid-coloured fabric it the side where the dotted pricks at the selvedge feel smooth on touching. For printed fabric, it the side of the fabric where the prints appear brighter.
Rise: The measure between the waist band and the crotch seam on pants.
Rolled hem: The edge of garment is rolled and stitched for a very narrow hem.

## Slide 47
Rubber ring: This is a ring on the bobbin winder which comes in contact with the nut of the balance wheel.
Ruffles: It is a pleated piece of fabric often used as trim on clothes.

## Slide 48
Seam: A line along which two or more fabrics are joined by fusion, gluing, sewing, stapling. Usually near edges of the fabric pieces.
Seam allowance: It is the area between the edge and the stitching line on two (or more) pieces of material being stitched together.
Seam finish: Any technique that finishes the raw edges of a seam.
S

## Slide 49
Seam roll: It is a cylindrical-shaped long tool used to press open long seams or to slide inside a sleeve for creaseless pressing.
Selvedge: The edge of fabric that runs parallel to the warp (lengthwise) yarns is called selvedge.
Set-in sleeve: A sleeve sewn into an armhole or armscye .

## Slide 50
Sewing needle: It is a fine cylindrical piece of metal with a sharp point at the lower end, a hole or eye in it, used in sewing.
Sewing threads: It refers to special types of yarns that are designed to pass through a sewing machine.
Shank: The back of a button through which the thread passes, to attach the button to the garment

## Slide 51
Shears: It is a cutting instrument with two blades like scissors, typically larger and heavier.
Sheer: Any transparent or very light-weight fabric as sheer chiffon, crepe, georgette or voile of various constructions and yarns.
Shirring: It is a process to gather (an area of fabric or part of a garment) by means of drawn or elasticized threads in parallel rows

## Slide 52
Shuttle: It holds the bobbin case and moves to form the loop as the machine is operated. It is fitted below the feed dog.
Skipped stitches: In skipped stitches, there is no needle thread or looper thread movement for a portions of the stitch cycle.
Sleeve board: Small ironing board that fits inside a sleeve.
Sleeve cap: The area of the sleeve above the biceps line. This passes over armhole edge on the shoulder.

## Slide 53
Slit: An open part of a seam often found in skirt side or center back seams and also in kurta side seam.
Slip stitch: It is used to join two folded edges or one folded edge to a flat surface, for an almost invisible stitch.
Snagging: It is the defect in fabrics where a yarn or part of a yarn gets pulled or plucked from the surface
Snap tape: It is a narrow strip of fabric usually twill weave with a continuous row of snap fasteners, sometimes called press studs.

## Slide 54
Staple yarn: Short length yarns produced from short-length fibers are called staple yarns.
Stay stitch: Stitching placed on or just outside the seam line, used to stabilize the fabric
Stitch: Loop or loops of one or more threads when bound with each other, either by inter-looping or interlacing, sewing fabric.

## Slide 55
Stitches per inch (SPI): A stitch per inch(SPI) is measured by counting the number of stitches found within one inch.
Stitch length: Length of a stitch determined by the movement of the feed dog.
Stitch line: It refers to a line in the paper pattern where one complete movement of a threaded needle passes through a fabric or material over the line.

## Slide 56
Strand: A general term for one component of a rope, thread, or ply yarn, or any of the fibers that are twisted or plaited together.
Stretch fabric: A property of fabric in which elongation (stretching) and recovery to its original position is measured.
Stripe: A design consisting of bends or straight lines against a plain background

## Slide 57
Tacking: Fastening pieces of fabric together, mostly temporarily, with stitches
Tassels: A bunch of loosely hanging threads or cords knotted at one end and attach for decoration of garments.
Terry: It is a woven fabric, usually cotton, or a blend with man-made fiber, with loop pile on one or both sides.
T

## Slide 58
Thread tail: The left-out thread, unfinished or untrimmed threads on the edges
Thread tension: The degree of tightness of stitches in machine sewing or the state of the thread being stretched tight
Top stitch: It is a row of continuous stitches on the top or right side of a garment or any other article.
Trim: It is any decorative item, ribbon, lace, etc., that is put on a garment or other item that is being sewn.

## Slide 59
Trimming materials: Additional material used for decorative or functional purposes on a garment.
True bias: Also called true across, it refers to a of 45 degrees angle that intersects the warp and weft yarns in a woven fabric.
Tucks: These are folds of fabric which are stitched in place by straight rows of machine stitching.
Twill weave: It is a type of plain weave with a pattern of diagonal parallel ribs.

## Slide 60
Under lap: The lower fabric of two overlapped pieces of fabric.
Underlay: A layer of fabric or thin material below another layer of fabric.
Underlining: Light weight fabric placed inside the garment to hold the shape of the fabric/garment or support its strength.
Upholstery fabric: Any fabric used as upholstery, made with a wide variety of fibers including cotton, linen, silk, wool, man-made fibers, etc.
U

## Slide 61
Velvet: It is a warp ply fabric with short closely woven cut pile that gives the fabric a rich, soft texture.
Vent: A slit in the back hem of a jacket, which allows the wearer, to move, bend, sit.
Voile: It is a lightweight, sheer fabric, made of hard twisted yarns in a low count plain weave. It is made of cotton, worsted, silk, rayon or acetate.
V

## Slide 62
Warp: It is the lengthwise yarns used in the weaving operation.
Worsted: The fabric made from yarns spun wholly from combed wool are known as worsted fabrics.
Wrong side of the fabric: For a solid-colored fabric it the side where the dotted pricks at the selvedge feel raised on touching. For printed fabric, it the side of the fabric where the prints appear dull and faded.
W

## Slide 63
Yarn: It is a continuous strand of textile fibers that may be composed of endless filaments or shorter fibers twisted or otherwise held together.
Yardage: The length of fabric that is required to cut all pattern pieces of a garment is called yardage.
Yoke: It is a shaped pattern piece which forms part of a garment, usually fitting around the neck, shoulders, or around the hips to provide support for looser parts.
Y

## Slide 64
Zigzag stitch: The Z-shaped stitches used to finish raw edges. It may be used for decoration purpose also.
Z

## Slide 65: Summary
In this session you have learnt about terminologies related to garment.

## Slide 66: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma