## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 3: BASICS OF GARMENT CONSTRUCTION
Session 5: Fasteners, Plackets And Trims

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Types of fasteners | 6
Summary | 24

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about various types of fasteners, the purpose of using fasteners.
Explain about plackets and its types.

## Slide 5: ABOUT FASTENERS, PLACKETS & TRIMS
A fastener is a tool that is used to close and open a opening in a garment. These are also known closures.
A placket is an opening in the garment which aids in easy slip on and slip off garments on body.
Trims are used as a part of garment design to enhance its overall look without overpowering it.

## Slide 6: TYPES OF FASTENERS
Hooks and Eyes
Hook: Hooks are sewn with the help of overcasting stitches around the rings and across the bar of the hook.

## Slide 7
Eye: It is of two types
Metal Eye: Metal eyes are stitched with the help of buttonhole stitches around the rings along the fabric.
Thread Eye: It is done by marking two points by positioning the hook. A thread eye is sewn as long as the space between its two placements marks.

## Slide 8
2. Buttons: Buttons are used for both decorative and functional purpose. They are made from a variety of material and can be sewn with the help of machine or hand.
Sewing buttons with holes: Button with holes comes in variety of sizes and are expressed with term ligne or L.
Sewing fancy or shank buttons: Shank buttons have a circular extension on the back through which the button is attached with thread.

## Slide 9
Sewing Press Buttons or Snaps: Press buttons or Snaps are a kind of small fasteners having less holding power than hooks and eyes.
It has two parts – a ball and a socket.
The socket is placed on the underlap of the placket while the ball is attached to the overlap of the placket.

## Slide 10
Buttonholes: Buttonholes are slits cut in garments to hold buttons in place. Button holes are worked on the overlap before the buttons are fixed. There are two types of buttonholes:
Worked Buttonholes: These are made by hand or by machine on the face of the garment after the garment is completed.
Bound Buttonholes: These are made of separate strips of fabric and are suitable for jackets, coats, sherwani, woollen dresses.

## Slide 11
Button Loops: They are made of bias tubing, thread or cord and are placed in the seam or fold edge.

## Slide 12
Eyelets: Eyelets are mainly used for lacing front openings decoratively.
To make an eyelet cut a circular hole and work buttonhole stitches around it.

## Slide 13
Zippers: It is a fastener that has two rows of metal or plastic teeth on a strips or binding and a slider that closes an opens the teeth.
Skirt zipper: It is available in 7 or 9-inch length and opens at the top.
Dress zipper: It is closed at the upper edge with a bridge top stop, available in 10, 12 and 14-inch lengths.
Neckline zipper: It opens at the top and used for necklines, sleeves, housecoats or underarm blouse plackets.

## Slide 14
Plackets: It are an opening in upper or lower part of the garment that aid in putting on or removing garment easily. Following are the types of placket.
French placket
Concealed placket
Classic front placket
Bound placket
Partial button placket

## Slide 15
French placket: The placket edge is folded inwards and so that no stitching is visible on the outside of the garment. This gives the placket a tidy appearance. These are commonly found in shirts.
Concealed placket: A concealed placket is a placket where the fasteners are hidden under the top layer of the placket.
Classic front placket: A classic front is a sort of placket in which the cloth is folded and sewn to give a visible strip of elevated cloth, or a separate strip is added to create a placket.

## Slide 16
Bound placket: A bound placket is a type of placket which is added in the garment as a finished edge of a slit. These are generally seen in sleeves, children wear, women’s wear.
Partial button placket: A partial button placket is a type of placket which extends to a short distance instead of full length of the garment. This is generally seen in kurta.

## Slide 17: CONSTRUCTION PROCESS OF PLACKET
Sample size- 6inch X 6inch
Placket fold- 1inch
Placket extension- 0.5inch

## Slide 18: PLACKET PREPARATION PROCESS
Take a sample of 6inch X 6inch.
Divide the width of the sample into two equal parts i.e 3inch each.
The size of each piece is 3inch X 6inch.
On the wrong side of fabric of one piece mark it as right side and mark other as left side.
Mark placket extension line on both the pieces 1.5 inches from the edge as.
Mark placket fold line 1 inches from the outer edge.
Now, mark the button line and hem line on the placket fold.

## Slide 19: PLACKET CONSTRUCTION PROCESS
Fold the pieces on the wrong side at the placket fold line.
Place the folded pieces (Right over Left).
Make sure that the button of both the pieces coincide each other.
Finish the placket by hem stitching at the ¼ inch mark from the outer edge of the placket fold.
Attach buttons on the button line of right side of placket and make buttonholes on the button line of left side of the placket.

## Slide 20
9. Trims: Trimming material is the material used to provide functionality and/or decoration to the garments or any other article. Following are the types of trims.
These are used to add design element to the garment.
It is a soft trim used at various places to create emphasis.
These are used at the necklines, sleeves edges, borders, etc.
Tassels

## Slide 21
The term lace refers to the type of open structure.
Lace is used both for decorative & functional element
Scalloped edge laces are also available
Laces are used in top, dresses, lingerie, napkins, handkerchiefs etc.
Laces are soft trims.
ii. Laces

## Slide 22
Braids are both detachable and fixed
Braids are narrow flat fabric or narrow tube structures similar to shoe laces.
Braids are produced by interlacing yarn/twisted fabric diagonally in a form of plaiting.
Can be used in binding around medium & heavy weight garments.
Can be made from polyester, wool and acrylic.
iii. Braids

## Slide 23
Binding: bindings are functional trims and are used to the finishing of edge of the garment, like hem finishing, necklines, armholes, opening.
Edgings: Edging are applied on the edge in the garments like hem, ruffles, piping, laces, ribbons, tapes, etc.

## Slide 24: Summary
In this session you have learnt about various types of fasteners, the purpose of using fasteners and plackets and its types.

## Slide 25: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma