## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 2: SEWING TOOLS & SEWING MACHINE OPERATIONS
Session 4: Preparation and operation of Sewing machine

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Preparation of single needle sewing machine | 5
Summary | 22

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about preparation of single needle sewing machine

## Slide 5: PREPARATION OF SINGLE NEEDLE SEWING MACHINE
Connect the machine to the power supply
Placement of foot control
Adjust the presser foot
Wind the bobbin
Select the correct needle and thread for sewing
Fix the needle into needle bar
Set the bobbin and bobbin case in the machine
Thread the machine
Adjust the thread tension
Adjust the stitch length
Check the stitch formation
Check the reverse stitching lever

## Slide 6: Connect the machine to the
Before connecting the power cord, ensure that the voltage and the frequency shown on the sewing machine conform to the electrical power.
Connect the plug to connect the foot control.
Now, connect the foot control to the machine socket.
Connect the power plug to the power socket.
Switch ON the power and sewing light.

## Slide 7: Placement of foot control
The speed of the sewing machine can be controlled by the foot control. The stronger it is pressed on the control, the faster the machine runs.
The foot control should be placed at the correct position for the tailor to operate it comfortably.
Note: This step is applicable for a motorized sewing machine.

## Slide 8: Adjust the pressure of the presser foot
It is important for a tailor to have complete knowledge of the required pressure on the material.
The pressure of the presser foot can be adjusted by using the thumbscrew.
To increase the pressure, turn the thumbscrew clockwise or downward. To lighten the pressure, turn the thumbscrew anticlockwise.

## Slide 9: Wind the bobbin
The following steps are to be followed to fill the bobbin:
Place the bobbin spool on the bobbin winder fitted on the top.
Wrap the thread from the reel placed in the thread spool around the bobbin.
Press the treadle/foot control or turn the hand wheel to start winding.
The winding in the bobbin should be uniform.
Once the bobbin is sufficiently filled with thread, stop winding and remove the bobbin.

## Slide 10: Fix needle into the needle bar
Pull the needle bar to the highest level to insert the needle.
Loosen the screw or needle clamp to fix the needle.
Insert the needle in a straight line in the groove and tighten the needle clamp securely and tightly to fix the needle properly.
If you are still having trouble, refer to your machine’s manual.

## Slide 11: Set the bobbin and bobbin case in the machine
Hold the wound bobbin and bobbin case with both hands.
Place the bobbin in the bobbin case correctly.
Pass the thread through a small notch at the front of the bobbin case and then pull the thread out.
See that the bobbin should move clockwise when the thread is pulled out.
Leave the end of the thread outside the bobbin case.
It should be brought up through the hole in the throat plate after the top thread is threaded.
Hold the latch of the bobbin case and fix into the rotary hook
Lock the bobbin case in the machine.

## Slide 12: Thread the machine
Follow the instruction to thread as per the guidelines printed in your machine’s manual.
The take-up lever should be raised to keep the needle at its highest point which will help in threading the upper thread.
Place the thread reel on the spool pin
Take the thread end with the hand and pull it through the thread guide at the top
Now pull the thread down and wrap it around the tension knob
Pull the thread back up again at the second thread guide
Thread the needle from front to back.
Usually, the thread follows this general pattern: left, down, into a hook, through the needle.

## Slide 13: Adjust thread tension
The tension of the stitch is regulated by two controls.
Upper thread tension
After lowering the presser foot, turn the nut to the left to loosen it and to the right to tighten the tension.
Lower thread tension
It is adjusted by tightening/loosening the screw of the bobbin case
2
Lower thread

## Slide 14: Adjust the stitch length
A stitch length regulator/dial is used to adjust the stitch length and get the desired length.
The stitch length regulator/dial controls the distance that the feed dogs move the fabric to the back of the machine to make a single stitch.

## Slide 15: 10. Checking the stitch formation
The needle descend (that is, the downward action of the needle) through the fabric.
It reaches its lowest point and begins to rise slowly.
It creates a loop. The shuttle enters the slack-loop, enlarging it and taking with it the under thread.
When the needle reaches back to its highest level, a complete interlock stitch is formed.

## Slide 16: Steps of stitch formation illustration

## Slide 17: Checking of reverse stitching lever
When the reverse stitching lever is pushed, the cloth feed direction for sewing will be reversed.
When it is returned to its original position, the feed direction for sewing will change back to normal.

## Slide 18: OPERATING THE SEWING MACHINE
Single needle sewing machines are mostly used in domestic tailoring and also in industrial or commercial production.
They are most commonly used as they serve the purpose of basic seam formation.
The stitch is formed by interlocking two threads - the upper and the lower bobbin thread.

## Slide 19: 1. Sew on the fabric
Raise the presser foot and take the take-up lever is at its highest level.
Pull the upper and lower threads to the backside under the presser foot to avoid knotting.
Turn the flywheel until the needle point enters the fabric at the exact beginning point.
Lower the presser foot and then start the machine slowly.
To check stitch length and proper tension, first stitch on a rough cloth.
Gradually, increase the speed of the sewing machine for stitching.
The fabric will move forward and the stitch will be formed continuously.
Before the end, stitch slowly with the right hand on the fly wheel & left hand on the fabric.
Take the presser up , & pull the fabric with threads to avoid bending of the needle.
Cut the threads using the thread cutter or scissors.
Place the fabric to be stitched under the presser foot.

## Slide 20: PRECAUTION
Do not pull the material/fabric forward or backward, but hold the two layers slightly tight and firm at the back and front of the presser foot.
Keep the take-up lever at its highest point to avoid unthreading the needle when beginning to stitch again.
Leave about two to four inches of thread, extending from the machine to prevent unthreading.

## Slide 21: 2. Fastening the thread ends
This can be done in three ways.
Reverse stitching - Stitch till the termination point with the needle in the fabric. Now carry out reverse stitching, and then cut the threads.
Pivoting - Stitch till the termination point with the needle in the fabric, lift the presser foot and stitch back a small distance along the seam. Cut the threads
Tying - After reaching the end of the stitching line, pull the fabric back and cut the threads, leaving about two to four inches. Pick the last stitch with a pin or needle point and then tie a double knot.

## Slide 22: Summary
in this session you have learnt about preparation of single needle sewing machine.

## Slide 23: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma