## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 3: BASICS OF GARMENT CONSTRUCTION
Session 4: Disposal of Fullness

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Methods to add fullness | 5
Summary | 15

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about adding fullness in garments through, pleats, darts, tucks, and gathers.

## Slide 5: FULLNESS
Fullness is introduced into garments for various reasons such as:
To give good shape
Proper fit to the garment
To allow freedom of movement
Comfort to the wearer
To make the garment look attractive

## Slide 6: METHODS TO INTRODUCE FULLNESS
Pleats: Pleats provide fullness by adding folds in the garment.
They can be placed single or in a series and can be pressed flat or left un-pressed, according to the style of the garment.

## Slide 7: TYPES OF PLEATS
Knife pleats
Knife pleats are ½ to 1 inch wide and are turned towards the same direction.
Box pleats
Two knife pleats when turned away from each other (one to the left and one to the right) form a box pleat.
Inverted pleat
It is made up of two knife pleats turned towards each other so that the folds meet in the middle on the right side of the garment.

## Slide 8
Darts: Darts are a type folds that are used to shape a flat piece of fabric to fit the curves of the body. Following are the types of dart:
Single Pointed Dart/Standard dart:
It is a triangular, open shaped dart that is mostly used at bust and waist area of the garment.
Double Pointed Dart/Fish-eyed dart:
This dart is created, when two standard darts join each other at the widest ends. It is mostly found in jackets and dresses to give fit at the waist while shaping hips and busts

## Slide 9
Tuck: These are folds of the fabric which are stitched in place by straight rows of machine stitching.
A tuck is similar to a pleat the only difference between a pleat and tuck is that a tuck is stitched at the base to keep the fold secure.
It is introduce in a garment to:
Shape the garment according to the body
Add in fullness
Add decorative effect on shoulders, waistlines, yokes, pockets or cuff of sleeves etc.

## Slide 10: TYPES OF TUCKS
Pin tucks: These tucks are, fold along the middle of the markings and tacked or machine baste about 2mm wide from the fold.
Piped or corded tucks: These are made by placing cord on the wrong side of the fabric at center of tuck before stitching the tuck.
Cross tucks: When rows of tucks are stitched along the fabric in both horizontal and vertical directions, it is called cross tucking.

## Slide 11
Gathers: Gathering is an effective and decorative way of distributing fullness over a given area.
Gathers are folds of fabric that provide fullness, which are created using machine or hand stitches.
These are formed by drawing the fabric together on a line of stitching.

## Slide 12: DEVICE TO CREATE GATHERS
Gathering by machine
Gathering by hand
Gathering by using elastic

## Slide 13
5. Shirring: When several rows of gathering (3 or more) are used for a decorative finish it is termed as shirring.
It can be done at the shoulder, waistline, at the lower edge of a sleeve and usually at the narrower parts of garment.
Shirring can be done by these methods:
Thread shirrs – Thread is used to form gathers
Elasticized shirrs – Elastic is used to form gathers.

## Slide 14: Summary
In this session you have learnt about adding fullness in garments through, pleats, darts, tucks, and gathers.

## Slide 15: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma