## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 5: CONSTRUCTION OF GARMENTS FOR CHILDREN AND FEMALES
Session 6: Drafting And Construction Of A Salwar, Kurta And A Blouse

## Slide 3: Content
Title | Slide no.
Session objectives | 4
Construction and drafting of salwar | 5
Construction and drafting of kurta | 11
Construction and drafting of blouse | 19
Summary | 25

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about drafting and steps of construction of salwar, kurta and blouse

## Slide 5: 1. SALWAR
Salwars can be made in different patterns, like, belt salwar, plain salwar, Patiala and so on.
There is different variation of salwar for e.g., dhoti salwar, Patiala salwar etc.

## Slide 6
Measurements
Full Length = 40”
Lower waist = 30”
Hip = 36”
This garment requires 2 waist pieces (belt or upper portion of salwar); 2 center pieces; 4 side pieces(kalis) and 2 separate pieces for finishing the bottom of salwar with interfacing.

## Slide 7
Measurements
Full Length = 40”
Lower waist = 30”
Hip = 36”
This garment requires 2 waist pieces (belt or upper portion of salwar); 2 center pieces; 4 side pieces(kalis) and 2 separate pieces for finishing the bottom of salwar with interfacing.
Instructions for Drafting
Belt/Waist pieces
0 – 2 = ½ of round hip + 3”
0 – 1 = 10” (includes seam allowance and fold allowance)

## Slide 8
Lower portion of salwar
4 – 5 = (center panel) full length – belt + 2” (40 – 8 + 2 = 34”)
5 – 7 & 4 – 6 = 13” (standard)
8 – 10 = 12” (side piece or kali)
10 – 11 = 7”
8 – 9 = 34” (same length as center panel/kali)
9 – 13 = 1”
Join 13 – 11,
Cut 2 pieces of fabric of belt
Cut 2 pieces of fabric of center panel
Cut 4 pieces of fabric of side piece

## Slide 9
Stitching process
Join the center panel 6-7 with side panel of 8-9 on one side and for other side join the second side piece (kali) with center panel with 4-5. Repeat the same for the other leg portion.
After completing the stitching of both the leg potion of salwar.
Take the gathers at the waist line at front only by keeping the machine at number 5 for long stitches.
After putting the gathers at the lower portion of the salwar it is than joined with belt the upper portion of the salwar.
Join the leg seams of both the left and right sides separately.
Complete stitching of the upper portion and folded at the waist 2” and insert a cloth tape or elastic.

## Slide 10
Salwar on single fold

## Slide 11: 2. KURTA
It is perhaps the favourite outfit in India both for males and females, though its size and shape keep on changing according to the fashion.
It is a comfortable dress worn in all seasons especially in the summers for comfort.
It is worn with the combination of salwar, churidar, dhoti, lungi and even jeans.

## Slide 12
Measurements
Full Length = 40”
Waist length = 15 1/2”
Shoulder width = 14”
Bust = 34”
Waist = 28”
Hip = 36”
Armhole = 15”

## Slide 13
Pattern parts Required
Front cut 1 piece on fold, back cut 1 piece on fold, sleeve cut 2pieces.
Material suggested
Cotton, poplin, silk, crape, woolen, synthetic, chiffon crepe and satin.
Material Required
2.50 meter. Cloth width 42”

## Slide 14
Drafting of kurta
1 – 2 = full length + 2”
1-6, 3- 7 = ½ of shoulder
1-3, 6-7 = ½ of armhole
3- 8 = ¼ bust + 1 ½ “(ease)
1-4 = waist length
4 – 15 = ¼ of waist + 1 ½ (ease)
2 – 16 = ¼ of hip +3”
Join 8 -15- 17 for side seam
16 – 17 = 1”
Join 17 to 2

## Slide 15
Neckline for kurta
1-10 = 3 ½” (as per requirement 2” – 6”)
1 – 21 = 2” (as per requirement 2” – 6”)
1 – 5, 6 – 7 (as per requirement and shape of neckline)
Shape the back neck by joining 21 – 10
Shape the front neck by joining 5 – 10
6 – 9 = ¾”
Join 9 – 10 for shoulder slope.
19 is center point of 6 – 7
19 – 20 = ¾”
7 – 18 = 1”. Give a curve to front armhole by joining 9 – 20 – 18- 8
Give a curve to back armhole by joining 9 – 19 – 8

## Slide 16
Darts
Darts can be used as per the requirement of the waistline the total length of dart is 8’ length 1” width (4” towards the bust and 4” towards the hip)

## Slide 17
Sleeve
0 -1, 2 – 3 = 7”
1– 3, 0 -2 = ½ of around the arm
2– 4 = 4”. Join 4 to 0.
5 is the centre point.
5 – 6 = ¾”
5 – 7 = ½”
Give a curve to front armhole 0 -7 -4.
Give a curve to back armhole 0 -6 -4.
1– 8 = ½ of armhole + 1”
Join 8 – 4
Fold allowance is 1” included in the sleeves.

## Slide 18: Steps of construction/ stitching process
Join the shoulders
Finish the front and back neckline using a facing.
Give side seams leaving the slit area
Finish the sleeve by joining its sides and lower turning
Join the sleeve to the kurta sides
Finish the slits and lower turning of kurta

## Slide 19: 3. BLOUSE
The sari blouse combination is worn by women since ancient time though its designs, necklines and sleeve length and shapes kept on changing according to fashion.
A plain blouse can be adapted to various designs for e.g., choli-cut blouse, katori blouses etc.
Other than sari, it is also worn with ghagara or lehnga.

## Slide 20
Measurements
Drafting of plain blouse with V neckline, plain sleeves and opening can be kept either at the front or at the back.
Bust = 32’’
Waist = 28’’
Shoulder = 14’’
Length = 14’’ +1”
Sleeve Length = 10” + 1 ½” (for fold)
Sleeve width= ½ of around the arm + 1”
Armhole = 15”

## Slide 21
Instructions for Drafting
0 -2 = Full length + ½” for back
0 – 13 = Full length + 1” for front
0 – 5 & 1 – 6 = ½ of shoulder =7”
0 – 1 &5 - 6 = ½ of armhole
1 – 9 = ¼ bust + 1 ½”
0 – 3 = 3 ½”
0 – 17 = 2” (as per requirement 2” to 6”)
0 – 4 = 6 to 7” (as per requirement)
Shape back neckline by joining 3 to 17
Shape front neckline by joining 3 to 4
5 – 7 = ¾”

## Slide 22
Join 7 – 3 for shoulder slope.
18 is the centre point of 5 – 6
6 – 8 = 1”
18 – 19 = ¾”
Give a curve to front armhole 7 -19-8-9
Give a curve to back armhole 7-18-9
2- 11 = ¼ of waist +2”
11 – 12 &2- 13 = 1” for front bodice
Join 12 – 13 for front bodice
Join 2-10 for back bodice

## Slide 23
Darts
13 – 14 = 4” Dart width is 1” (½” on each side)
14 – 20 = 4” (waist dart)
20 – 21, 21 – 22, 22 – 23 = 1”
Draw centre front dart from 21 – 16 = dart width is ½” (¼”on each side)
9 – 15 = 5” (side seam dart)
Join 15 – 22. Dart width is ½”(¼” on each side)
Join 8 to 23. (armhole dart) Dart width is ½”( ¼” on each side)
Sleeves
Same as the sleeves given in the draft of kurta

## Slide 24
Steps of construction and the stitching process
Join the shoulders
Finish the front and back neckline using a facing.
Give the dart seams
Give side seams of the blouse
Finish the sleeve by joining its sides and lower turning
Join the sleeve to the kurta sides
Finish the lower turning of blouse using a braid.

## Slide 25: Summary
In this session you have learnt about drafting and steps of construction of salwar, kurta and blouse

## Slide 26: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma