## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 2: SEWING TOOLS & SEWING MACHINE OPERATIONS
Session 3: Needles And Threads

## Slide 3: Content
Title | Slide No.
Session Objectives | 4
Needle and its classifications | 5
Sewing threads and its type | 20
Selection of sewing thread and needle | 24
Summary | 26

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about sewing machine needles and parts of a needle, types of needles.
Explain about choosing appropriate needle and thread for fabric.

## Slide 5: HAND SEWING NEEDLES
Hand sewing needles are used for hand sewing or embroidery.
Needles are mostly available in different sizes, from small size 9 to the heavy size 18.

## Slide 6: TYPES OF HAND NEEDLE
Milliner needles are long needles used for tacking or basting.
Sharp needles are medium length needles used on all types of fabric for hand sewing.
Between needles are small, short length needles used for fine stitches.

## Slide 7: PARTS OF HAND SEWING NEEDLE
Eye
Point
Stem

## Slide 8: SEWING MACHINE NEEDLES
Machine needles are specialised needle mainly used in sewing machine for sewing purpose.
Each manufacturer of the needle identifies its needles in a different way; and needles for the same type of system may have several different names or numbers, depending on the manufacturer.

## Slide 9: FUNCTIONS OF A SEWING NEEDLE
To produce pathway in the fabric and enable the sewing thread to pass through.
Carry the sewing thread through the fabric and make a loop

## Slide 10: PARTS OF A SEWING MACHINE NEEDLE
Butt: A small pyramid structure at the bottom to fit in the hole on the needle bar.
Shank: A round structure clamped at the needle bar to support needle blade.
Shoulder : The beginning of the shank just above the needle blade.
Blade: A thin section of the sewing needle that extends from the shank to the eye.
Short groove: It is a small groove between the tip and the needle eye.

## Slide 11
Scarf: It is a small indentation above the eye that permits the hook to pick up the thread loop.
Point: It is the tapered end of the needle and is often considered the most critical part of the needle.
Eye: An opening in the needle blade that carries the thread.

## Slide 12: NEEDLES CLASSIFICATION
Types of Needles
General Purpose Needles
Specialty Needles

## Slide 13: GENERAL PURPOSE NEEDLE
Universal point needles: A general purpose needle that is both sharp and round to sew different types of fabric.
Sharp/microtex needles: A sharp slip needle, used for stitching silk, light weight and micro fiber woven fabrics.
Ball point needles: A general-purpose needle, slightly rounded point used for stitching knitted fabrics.

## Slide 14: TYPES OF BALL POINT NEEDLE
Light Ball Point: Used for sewing lightweight knitted fabric.
Medium Ball Point: Used for sewing medium weight knitted fabric.
Heavy Ball Point: Used for coarse knitwear and for sewing dense woven elastic.
Special ball point: Used for medium to course elastic materials with covered elastomeric threads and very coarse knitwear.

## Slide 15: SPECIALTY NEEDLES
Jeans/denim needle: These are designed to sew closely woven fabrics such as denim, canvas and multiple fabric layers.
Top stitch needle: These are very sharp needles that have deeper front groove and an extra-large eye to accommodate top stitching thread.
Quilting needles: These needles are thin and tapered with sharp point and are used for stitching multiple layers.

## Slide 16
Hem stitch/wing needle: The sides of hem stitch needle’s shank are flared like wings. That is why it is also called wing needle.
Leather needle: These needles have wedge shaped point which pierces real leather, vinyl and suede, creating small stitch holes and strong seams.
Stretch needle: This needle is designed particularly for the knits having spandex, lycra as well as synthetic suedes as they prevent skipped stitch.

## Slide 17
Metallic needle: Special designed to stitch with metallic threads, these needle’s have large eye, special longer scarf to prevent skipped stitches and large and deep groove to prevent shredding of delicate metallic and decorative threads during stitching.
Machine embroidery needle: They are designed with a large eye and special scarf that protects fragile threads and prevent shredding and breakage while sewing with rayon and embroidery threads.

## Slide 18
Self-threading needle: This needle have slip in threading slot to help in the threading process.
Spring needle: These needles have a wire cage above the needle point to prevent the fabrics form riding onto the needle when presser foot is removed and the feed dogs are dropped for free motion stitching.
Double/ twin needles: Arrangement of two needles on single shaft produce two rows of stitches and are used for top stitching, pin tucking and decorative stitching.

## Slide 19
Double/ twin needles: Arrangement of two needles on single shaft produce two rows of stitches and are used for top stitching, pin tucking and decorative stitching.

## Slide 20: SEWING THREAD
Sewing threads are designed to pass through a sewing machine and are capable of forming efficient stitches without breaking or becoming distorted during the useful life of the product.

## Slide 21: CLASSIFICATION OF SEWING THREADS
On the basis of substrate
Natural
Made from natural fibres
Example: cotton, silk, & wool threads
Synthetic
made of man-made fibres
Example: nylon, polyester, & thread

## Slide 22
On the basis of construction
Spun
These threads comprise of staple /spun fibers (short length).
Core Spun
These threads are combination of staple and filament fibers.
Filament
These threads comprise of filament fibers. They can be mono-filament (one single strand), multi-filament (two or more filaments) or textured filament.

## Slide 23
On the basis of finish
Water repellent
Flame proof
Anti-bacterial
Anti-mildew

## Slide 24: SELECTION OF SEWING THREAD AND NEEDLE
It is very important that the fabric and thread should share the same characteristics.
While wrong selection of thread may result in skipped stitches, broken seams etc. and can lead to monetary loss.
Therefore selection of threads and needle plays and important role in enhancing the overall appearance of the garment.

## Slide 25
S. No. | Type of Fabric | Type of Thread | Needle No.
1. | Lightweight: voile, chiffon, organza, fine lace. | Mercerized cotton, silk, nylon, extra fine (any fiber), size: 60–100 | 9 or 11
2. | Medium weight: crêpe, velvet, gingham, stretch fabric, terry, brocade, linen, corduroy, some types of denim. | Polyester, cotton-wrapped polyester, mercerized cotton, size: 50–60 | 11 or 14
3. | Heavy: wide rib corduroy, terry cloth. | Polyester, cotton-wrapped polyester, heavy duty (any fiber) size: 30-40 | 16 or 18
4. | Very heavy: canvas, upholstery fabric | Polyester, cotton-wrapped polyester, heavy duty (any fiber) size: 20 | 16 or 18

## Slide 26: Summary
In this session you have learnt about sewing machine needles for specialized machines, various parts of a needle, types of needles, choosing appropriate needle for fabric and machine, and thread classification.

## Slide 27: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma