## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 6: CARE AND MAINTENANCE OF SEWING MACHINE
Session 1: Cleaning, Oiling And Handling Of Sewing Machine

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Fabric selection | 5
Types of fabric used for garment construction | 7
Summary | 34

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge fabric selection and types of fabric used for garment construction.

## Slide 5: CLEANING, OILING AND HANDLING OF SEWING MACHINE
A clean, well-oiled sewing machine is essential for good output and safety.
Regular and proper cleaning, oiling, care and maintenance of sewing machine can help the tailor save time and money.
When not in use the machine must be kept covered with a suitable cover to prevent dust from settling on it.

## Slide 6: CLEANING OF SEWING MACHINE
While cleaning the machine, pay attention to the various parts of the machine, the machine table or stand, the work station, and even your hands, to avoid soiling the material being sewn, prevent accidents and damage to the machine.
Before attempting to clean the machine, it is wise to remove the needle to avoid the danger of sewing into the finger during the cleaning process.

## Slide 7: Material required for cleaning
Flat paintbrush (½" to ¾" wide)
Cleaning solvent or fluid
Soft disposable cloth
Screwdriver
Sewing machine manual
Small handy vacuum cleaner

## Slide 8: Points to be considered while cleaning
Before cleaning any machine it must be turned off.
Open the slide plate and remove the bobbin case. Then remove the throat plate. Whenever it is required, remove the face plate from the left end of the head.
Any lint, dust, or loose threads in the area around the feed dog and rotary hook, shuttle may be brushed or blown away.
Turn the hand wheel manually to expose any areas that might have been hidden initially. Brush again.

## Slide 9
Carefully tilt the machine head back until the head rests on the post on the back of the table.
Brush out any lint, dust, or threads from the lower part of the machine.
Use a soft, thin and clean cloth to remove any lint on the machine parts.
Unscrew all plates and screws and the bobbin case.
Check the needle to be sure it is clean and the eye is not clogged.
Replace the needle, if necessary.
Wipe away any excess oil or dust on the head, machine bed, motor, table, and stand.

## Slide 10
If there is lint between the tension discs and in the thread guides, use thread to floss the tension discs and remove any lint.
If you have oiled the machine, sew on few scraps to remove any excess oil.
Wash hands after cleaning and oiling the machine.
After completing the work, put a piece of fabric under the foot, lower the presser foot, cover the machine, and pick up any trash.
Remove only those parts that are detachable, and keep in mind the position and direction of each part that is removed for cleaning.

## Slide 11
When using a screwdriver, apply pressure on the screw, if a screw does not loosen easily.
Remove all the parts that is, the needle, presser foot, slide plate, throat plate, bobbin case, and the face plate. Put them in the tray and soak in cleaning fluid.
Wrap the motor to protect it from oil and cleaning solvent. Ensure that the sewing machine has been unplugged.
To clean the feed dog, remove the needle plate of the machine and brush off all lint deposits and dirt sticking to different parts.
To clean the shuttle case, remove all the screws holding the shuttle case. Take out the shuttle case and wipe its groove free of dirt, and thread bits.

## Slide 12
Thread bits must be removed which are caught in the wheel along with all lint and dust sticking to the treadle parts.
Use a cloth or small brush to clean near the needle and feed dog.
If the machine starts to run hard, it is an indication that dirt or lint is jammed inside a bearing. In that case remove the bobbin case and clean all lint and stray threads.
Use a dry brush to clean out all lint from bobbin case.
Remove bobbin and bobbin case, and clean small thread particles from there.

## Slide 13
Pull a piece of cloth soaked in the solvent, back and forth between the discs to clean it from dust, lint or any other particles.
Clean the hand wheel, washer, and the shaft. Lubricate the shaft with two drops of sewing machine oil and place a small amount of grease on all gears. Reassemble the hand wheel and clutch.
After properly cleaning these areas, reassemble all the parts of the sewing machine and run it.

## Slide 14: OILING THE SEWING MACHINE
Always keep your sewing machine well oiled.
All dust should be removed from the exposed parts at least once every week.
Always remove lint deposits, dust and thread bits before oiling any part of the machine.
In order to operate the machine smoothly, it is essential to oil it repeatedly.

## Slide 15: Material required
Sewing machine manual
Sewing machine oil
Soft disposable cloth

## Slide 16: Points to remember while oiling the sewing machine
Before oiling, ensure that the sewing machine is turned off.
Oil the machine using the directions given in the machine manual. Inspect the condition of all visible parts of the machine every time you oil it.
If a manual is not available, oil the machine as per the directions of the teacher/instructor as per the required frequency.

## Slide 17
Locate oil holes of the sewing machine and put one to two drops of oil into each hole. Turn the hand wheel manually so that the oil will work its way between the parts.
Wipe off all dust and excess oil from the machine or table; clean up any spilled oil immediately.
Sew on a few fabric scraps to remove any excess oil.
Wash hands after oiling the machine.

## Slide 18: Method for oiling of the sewing machine
It is necessary to oil the sewing machine periodically.
If the machine is used every day, oil it once a week.
If you do not use it very regularly, then oiling once a month is sufficient.

## Slide 19: To oil thoroughly keep the following point in mind
Remove the upper thread, needle plate, slide plate, face plate, bobbin case, and needle and presser foot.
Put sewing machine oil in all oil holes and joints where one part rubs against another.
While oiling, turn the fly wheel back and forth to facilitate the flow of the oil to different moving parts.
After oiling the points on the head of the machine, tilt the machine head back to oil the points on the underside.

## Slide 20
On a treadle machine, the belt will have to be released before tilting the machine head back. Remember to oil the pivots of the treadle.
When the machine has been completely oiled, wipe away excess oil and run it slowly for 2–3 minutes on a waste piece of material.
Before you close the machine, place a scrap of fabric under the presser foot and lower the needle. The fabric will absorb the excess oil and prevent the formation of oil spots on your work.
If the sewing machine becomes gummed and dirty with oil, put a drop of kerosene or petrol in each oil hole and at joints, and run it rapidly for 1–2 minutes.

## Slide 21
Wipe off the oil that oozes out with a soft cloth and re-oil the machine.
Check the machine instruction booklet/manual to determine the types of oil lubricant to use and where to use them.
Do not oil the tension discs, the hand wheel release or the belts and rubber rings in any machine.
Run the machine so the oil would be distributed into all the bearings.
For later oiling, one drop of oil on each bearing and in each oil hole is enough.
After oiling the sewing machine, wipe away the excess oil and reassemble the machine.

## Slide 22: CARE AND MAINTENANCE OF SEWING MACHINE
Most sewing machines encounter problems that can be traced to poor general maintenance or neglect.
But with some simple tools and just a few minutes daily, weekly, or monthly, depending on how much our sewing machine is used, we can help keep our machine running smoothly.

## Slide 23: Handling of sewing machine
Safe handling procedure of sewing machine
The safe handling procedure of the sewing machine involves:
Setting up of the sewing machine.
Adopting safety measures before starting sewing.
Adopting safety measures during sewing.

## Slide 24: Setting up of sewing machine
For setting up a sewing machine
Position the machine on a hard flat surface.
Select and install the needle securely into the needle bar.
Select the suitable thread according to the type of fabric to be used.
Wind the thread into the bobbin.
Following the thread guide, thread the machine from the spool pin to the needle.
Set the machine of required stitch length.
Balance the thread tension on the sewing machine (adjust the upper tension in relation to the lower tension).

## Slide 25
One must practice following safety measures before starting sewing:
The sewing machine cord must be in good condition. Switch off the sewing machine before threading the needle, and after every use, turn the machine off or unplug it.
Ensure that there is enough light while using the sewing machine. Using a sewing machine in poor lighting can lead to any accident or miss-happening.
Adopting safety measures before starting sewing

## Slide 26
Keep the feet off the treadle when setting or threading the needle.
Use the hand wheel to move the needle to its highest position while the fabric is placed for sewing.
One needs to hold the top and bottom loose thread ends before starting the machine.

## Slide 27: Adopting safety measures during sewing
A tailor must adopt following measures during sewing:
Practice on a scrap material to check against oil stains, etc.
Notice the way the sewing machine sounds. If the sewing machine makes some abnormal sounds or seems louder than usual, get it checked by a technical expert.
Sew at a slow, steady pace and use a needle guard to protect the fingers.

## Slide 28: Handling of material, tools and equipment
Handling of material
A tailor must consider following points while handling material:
Select appropriate needle, thread and stitch length suitable for the different type of fabrics.
Practice on the scrap material prior to starting work on the final fabric to avoid oil stains.
Also make a trial stitch on the waste fabric.

## Slide 29
Take care to set the presser foot in a way so as to hold the fabric in place.
Position the fabric on the machine in such a way that the larger portion of the fabric falls on the left hand side of the sewing machine.
Take care while sewing slippery fabrics, and if essential, use lining to give firmness to the slippery fabrics.

## Slide 30
Care and handling of tools and equipment
Following are guidelines for proper care and handling of different tools and equipments:
a. Measuring tape: It is used for taking body measurements and requires very little maintenance. The tape should be clean to check the accuracy of the markings. After each use, the measuring tape should be rolled or wrapped and kept in a clean box.
b. Sewing gauge: These are hand tools for measuring small areas during sewing. Select a jigsaw puzzle shaped gauge which will have markings for the most common sewing measurements. Do not allow the metal gauges to get bent.

## Slide 31
c. Pin cushions: These hold the pins and needles during working to prevent accidents while working. Select a standard pin cushion filled with fine sand, so that the abrasion of fillers may prevent the pins from dust and getting rusted.
d. Hand sewing needles: The needle should always be kept in a dry and clean case. To avoid damage to the point of the needle, it should not be pressed or pricked on a hard surface.
e. Sewing needle threader: The needle threader should have a large eye to hold the thread, as forcing the metal wire of the threader can cause it to break.

## Slide 32
f. Seam ripper: Keep the seam ripper sharp and clean, and use it only for sewing tasks. To prevent injuries and damage, keep the seam ripper covered when not in use.
g. Dressmaking shears: Use the shear for cutting fabrics and soft material only. If used on anything other than fabric, (thick sheet, etc.), it will reduce the sharpness of shear or cause causing uneven cutting, shredding of fabric and hand fatigue.
h. Pressing cloth: A press cloth is essential to protect the fabric from direct contact with a hot iron. It should always be clean and oil free for protecting the garment from oil and dust.

## Slide 33
i. Hams and sleeve rolls: Hams and sleeve rolls are wonderful for pressing curves. They should always be clean and oil free.

## Slide 34: Summary
In this session you have learnt about fabric selection and types of fabric used for garment construction.

## Slide 35: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma