## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 1: INTRODUCTION TO CLOTHING, TAILORING AND SEWING MACHINE
Session 3: Parts And Attachments Of A Sewing Machine

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Parts of sewing machines | 5
Attachment and their functions | 17
Summary | 23

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about parts of sewing machine and their function.
Explain about attachments and their functions.

## Slide 5: PARTS AND THEIR FUNCTIONS
A sewing machine has two major parts: upper part and lower part.
The upper part comprises of:

## Slide 6
Head: Head of the sewing machine comprises of complete sewing machine without the cabinet or stand.
Arm: It is the curved part of the sewing machine head. The arm contains mechanism for operating needle.
Bed: It is the flat portion of the sewing machine under the feed dog where it is mounted. The shuttle and lower thread are placed under the sewing machine bed.

## Slide 7
Lower part of the sewing machine comprises of treadle, legs etc. Presence of these lower parts depend on the type of machine.

## Slide 8: FUNCTIONS OF BASIC PARTS OF A SEWING MACHINE
Spool pin: An upright metal rod placed on top of the arm of the machine to hold the reel of thread.
Thread guide: A metal loop that takes the thread from the spool pin to the needle.
Tension disc: A combination of two concave discs placed together with the convex sides facing each other to control the delivery of the upper thread from the spool to the needle.

## Slide 9
Thread take-up lever: Fitted to the body of the arm and located above the tension disc, a lever pulls the thread back after each stitch, with an up and down motion so that it lays evenly over the fabric.
Needle bar: A metal rod which holds the needle with the help of a clamp to give motion to the needle.
Presser foot: It is a detachable device for holding the material in place on the feed dog while stitching.
Presser foot lifter: It is the lever attached to the presser bar to control the up and down movement of the presser foot.

## Slide 10
Stitch regulator: It controls the length of the stitch.
Bobbin winder: A device which helps in winding the bobbin (located inside the slide plate) properly.
Fly wheel (or balance wheel): A round wheel located at the right side of the sewing machine to controls the motion of the machine manually or electrically.
Slide plate: A rectangular plate, which facilitates the removal of the bobbin case without lifting the machine top.

## Slide 11
Needle plate or throat plate: A plate below the needle and presser foot on the machine bed with a small hole to allow the needle to pass through it.
Feed dog: A set of teeth fitted below the needle plate to move the material forward while sewing.
Face plate: A cover, which when removed, gives access to the oiling points on the needle bar, presser bar and take-up lever.
Arm: A horizontal part of the head that houses the drive shafts.

## Slide 12
Check spring: A small wire spring behind or at the top of the tension discs to provides tension on the thread of the needle and acts a shock absorber.
Slack thread regulator: A metal hook near the tension discs.
Bobbin case: A fixed shuttle case at the bottom chamber of the sewing machine that catches the top thread and form the stitch as the needle is lowered into the bobbin case.

## Slide 13
Clutch or thumb screw: It is in the center of the fly wheel and it engages and disengages the stitching mechanism.
Rubber ring: A ring on the bobbin winder which comes in contact with the nut of the balance wheel.
Bobbin winder tension angle: A device situated near the bobbin winder which helps to wind the bobbin evenly.
Needle clamp: A screw that is tightened to hold the needle in position.

## Slide 14
Handle driver: It is attached to the handle attachment of the machine and helps to drive it with hand.
Shuttle: It holds the bobbin case and moves to form the loop as the machine is operated.
Treadle drive: A large wheel located under the board in the treadle machine.
Treadle: A foot that rests at the base of the treadle machine which is pressed with the feet to operate the treadle machine.

## Slide 15
Pressure regulating screw: It is the screw above the presser bar, which can be tightened to increase the pressure on the fabric when stitching with fine/ lightweight fabric and loosened to accommodate thick fabric.

## Slide 17: ATTACHMENTS & THEIR FUNCTIONS
Blind hem foot: An additional attachment used for edge finishing of various apparels like trousers and skirts, and home furnishing items like curtains, etc.
Braiding foot: An attachment which is used in place of a presser foot while attaching braids, cords, elastics etc.

## Slide 18
Button fixing foot: The foot holds the button in place and then attaches the button to the fabric using zigzag stitch.
Buttonhole foot: It is used for preparing precise buttonholes or binding the raw edges.
Circular sewing attachment: It allows the operator to stitch in a circular pattern using straight stitch, zigzag stitch and any decorative stitches.

## Slide 19
Cording foot: To attach decorative cords and threads to the seam.
Decorative tape foot: This attachment is used to fix trimmings and ribbons on the fabric.
Gathering foot: It is attached to create gathers/ruffles on a fabric with high speed and precision.
Zigzag foot: It is attached to create designs in fabric using zigzag stitches of different widths

## Slide 20
Hemmer foot: It is used to stich the sleek and small edges of fabrics which automatically curls using either a straight stitch or decorative stitch.
Overcasting foot: It is used to make an accurate and consistent overcasting stitch where the thread is locked around the edge of the fabric and aligned with it to prevent the fabric from raveling.

## Slide 21
Ruffling foot: It easily makes and attaches ruffles on different types of fabric and finish the fabric edges.
Zipper foot: It is the foot used for attaching mainly zips and snap tape. Zipper foot has a narrow toe foot which gives more precision and visibility.
Elastic foot: It helps in attaching elastic to the fabric and provides even tension every time to avoid pulling and tugging on the needle.

## Slide 22
Darning foot: It is used for free hand embroidery and helps in proper stitch formation by keeping the fabric intact in the embroidery frame.
Overlock foot: It is useful for producing a durable finish on seams which are prone to fray easily or are bulky.

## Slide 23: Summary
In this session you have learnt about parts of sewing machine and their function and attachments and their functions.

## Slide 24: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma