## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 5: CONSTRUCTION OF GARMENTS FOR CHILDREN AND FEMALES
Session 4: Drafting And Construction Of A Baby Frock

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Layout of baby a frock | 5
Drafting of baby a frock | 8
Construction of baby frock | 15
Summary | 19

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about drafting and construction of baby a frock.

## Slide 5: LAYOUT OF A BABY FROCK
The layout for a frock with bodice and gathered skirt is shown below:
Back Bodice
Front Bodice
Front Skirt
Back Skirt

## Slide 6: Fabric marking of a baby frock
Lay out the pieces along the grain.
Secure the pattern, either with weights or pins. Weights do not ripple the pattern paper like pins do.
Using fabric marking tool trace around the pieces.
Mark all notches.
Now transfer darts and other details on the fabric by using carbon and tracing wheel or tailors chalk or any of the method.
Now the fabric is ready to cut.

## Slide 7: Fabric cutting of a baby frock
Fabric cutting scissors can be used to cut out the pattern pieces.
By taking care to align and cut your pieces accurately, will avoid mistakes later on during sewing.
Cut away the tracing line meant for cutting.

## Slide 8: DRAFTING OF A FROCK
This is stitched in one piece up to the knee length or top and skirt cut separately and stitched together.
The suitable fabric may be cotton, terry cotton, satin etc.
Its upper part is known as bodice or yoke and the lower part is the skirt.

## Slide 9
Fashion features
Pin tuck or lace on the front yoke.
Opening at back up to half the full length or up to full length.
Skirt joined to the yoke by gathering or tiny pleats.
Puffed sleeve.
Decorative stitches by coloured threads at the bottom round.

## Slide 10
Measurements
Chest (24”)
Shoulder (5”)
Bodice length (Yoke) (5”)
Frock length (22”)

## Slide 11
Instructions for drafting
Yoke drafting (upper portion of the frock)
1-2= yoke length =6”
1-3= ½ of shoulder=5”
1-4= 2 ½” (neck width)
1-6=1”
1-7= 3”
Give a shape to back neckline by joining 4-6
Give a shape to front neckline by joining 4-7
3-5=1/2”
Join 4-5 for shoulder slope
2-8=1-3 or ½ of shoulder

## Slide 12
8-9= ½”
Join 5-8 with a slight curve for front armhole
Join 5-9 for back armhole
2-10=1/2”
Join 2-8 for front yoke line
Join 10-9 for back yoke line

## Slide 13
Skirt drafting (lower portion of the frock)
Full length of frock less bodice length = skirt length
The bottom round of skirt is generally kept double the chest measure plus about 25 cm (10”).
Take two layers of material (the upper for the front and lower for back), with a fold at 11-12.
11-12 = Skirt length plus 2”

## Slide 14
11-13 and 12-14 = one- fourth chest, extra material for gathers or pleats.
13-15 = one-fourth chest plus 4 cm (1 ½”).
14-16 = one-fourth chest plus 6.5 cm (2 ½”) or 12-16 = one- fourth bottom round plus 1 cm (1/4”)
Join 15-16
16-17 = 1.5 cm(1/2”)
Shape bottom 14-17
15-18 = 2.5 cm (1”)
13-19 = same as 2 to 8 of bodice.
Shape front scye 19-18.
19-20 = 1.5 cm (1/2”). Shape back scye 20-18. Keep 5 to 10 cm (2 to 4”) below 12-14-17 for in turns.

## Slide 15: CONSTRUCTION FOR A FROCK
Neckline Finish
The neckline can be finished either with facing or binding. Here the frock is finished using shaped facing.
The shaped facing is cut to the exact shape of the garment edge to which it is applied leaving 1-1 ½” all around and cut.

## Slide 16
Place the Facing for front and back neck respectively on the neck. Make sure that the right sides of both the fabric are facing each other.
The pattern pieces for front and back should be interfaced. Match them up at the shoulder seams, pin together and stitch.

## Slide 17
Armhole finishes
The armhole can be finished either with facing or binding.
Attach placket at the back side of the frock
Place both the bodice (right sides facing) and complete by a side seam

## Slide 18
Skirt Finishing
Stitch the two-skirt piece together along the sides after forming gathers.
The finished look of Frock

## Slide 19: Summary
In this session you have learnt about drafting and construction of baby a frock.

## Slide 20: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma