## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 5: CONSTRUCTION OF GARMENTS FOR CHILDREN AND FEMALES
Session 5: Drafting And Construction Of A Plain Skirt, Petticoat And Nighty

## Slide 3: Content
Title | Slide no.
Session objectives | 4
Construction and drafting of plain skit | 5
Construction and drafting of plain skit six piece sari petticoat | 12
Construction and drafting of nighty | 16
Summary | 21

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about drafting and construction of baby a frock.

## Slide 5: PLAIN SKIRT
This skirt, with two darts at each side of back, is very popular nowadays.
It is plain at the waist, as there are no gathers at the belt-join.
If wider bottom is required, increase the bottom width accordingly.

## Slide 6
Measurement
Round Waist = 28”
Round Hip = 36”
Waist to Hip = 8”
Waist to Knee = 18”

## Slide 7
Back
Square both ways from 0
Skirt length + 2”
Waist to hip =8”
2-3= ¼thhip + 1½”
0-6 = ¼thwaist + 1½”
0 – 7 =1/2”
Join 6 and 7 with a curve
5-8 = 1”
Draw side Seam 6, 3, 8
Curve hipline outward and blend with 3 to 8
9 is midpoint of 6 and 7

## Slide 8
Construct a dart ¼” or ½” at this point and the length of the dart is 4”
Curve hemline ½” at point 8
Join 8-1 for hem line with a slight curve

## Slide 9
Front
Square both ways from 10
10 – 11= skirt Length +2”
10-12 = waist to Hip =8”
12-13 =1/4th hip + 1½”
10-16= 1/4th Waist + 1 ½”
10-17 = ½”
Join 16 and 17 with a curve

## Slide 10
15-18 = 1” Draw side seam 16,13,18
Give a curve at hip line & Blend with 13 to18
18-19 =1/2”
Join 19-11 for hemline
20 is midpoint of 16-17
Construct a dart width ½” or 1” & the Length of the dart is 4”

## Slide 11
Steps of construction
Stitch the darts
Join the front and back with a side seam leaving the placket opening at one side
Finish the placket
Join the waist belt with a backing
Finish the lower hemline.

## Slide 12: 2. Six piece sari petticoat
Petticoat is used inside a Sari. It is prepared with six pieces, which are narrow at the waist and broad at bottom.
If lace or frill is to be attached at bottom, reduce the length accordingly.
A casing (nefa) is attached at the waist, for inserting a cloth, drawstring (nadi).

## Slide 13
Measurements
Round waist = 28”
Round Hip = 36”
Full Length (waist to floor) = 40”
Casing Width = 1.5” or 2” (Belt)

## Slide 14
Instructions for drafting
0-1 & 2-3 = full length+2”
0-2 & 3-1 = ½ of round waist + 4”
0-4 = 1/12 of hip
3-5 = 1/6 of hip
Join 4 -5
4-6 & 5-7= ½”
Join 1-7 & 2-6 with a slight curve for lower hemline of petticoat.
Belt drafting
0-1 & 2-3= 2” width of the belt
0-2 & 1-3 = ½ of waist = 2” for length of the belt

## Slide 15
Steps of construction
Cut two center pieces and 4 side pieces (kali)
Join 1 center piece with 2 side pieces for both front and back
Give a top stitch to all six pieces
Join the side seams leaving space for placket opening at one side
Finish the placket
Attach the nefa/casing
Finish the lower turning of petticoat

## Slide 16: 3. NIGHTY
This is a loose-fitting garment which is worn during the night before going to bed that is why it is called nighty or night dress.
It is a chemise type of garment with or without sleeves. The full length varies according to choose.
Cotton fabric is preferred for nighties.

## Slide 17
Measurements
Chest 34”
Waist 28”
Full length 50”
Shoulder 14”
Hip 36”

## Slide 18
Instructions for drafting of an a-line nighty
0 – 2 = Full length + 2” (fold)
0 – 5, 1-6 = ½ of the shoulder
0-1, 5-6 = ½ of armhole
1- 9 = ¼ of bust + 2”
2 – 10= ¼ of hip + 3”
Join 9- 10, 10- 11 = 1”
Join 11 – 2

## Slide 19
Neckline
0 – 3 = 3 ½’’(standard)
0 – 12 = 1’’ (as per requirement)
0 -4 = 5” (as per requirement)
Shape back neckline by joining 3 – 12
Shape front neckline by joining 3 – 4
5 – 7 = ¾’’. Join 7 – 3 for shoulder slope.
8 is the centre point of 5 – 6.
8 – 13 = ¾”
6 – 14 = 1”
Give a curve to front armhole by joining 7 -13 -14 -9.
Give a curve to back armhole by joining 7 -8 -9.

## Slide 20
Sleeves
0 -1, 2 – 3 = 7”
1 – 3, 0 -2 = ½ of around the arm
2 – 4 = 4”. Join 4 to 0.
5 is the center point.
5 – 6 = ¾”
5 – 7 = ½”
Give a curve to front armhole 0 -7 -4.
Give a curve to back armhole 0 -6 -4.
1 – 8 = ½ of armhole + 1”
Join 8 – 4
Fold allowance is 1” included in the sleeves.

## Slide 21: Summary
In this session you have learnt about drafting and construction of baby a frock.

## Slide 22: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma