## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 4: MEASUREMENT TECHNIQUES
Session 1: Importance And Method Of Taking Body Measurements

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Body measurement and their importance | 6
Measurements needed for the construction of garments | 11
Precautions while taking body measurements | 32
Summary | 33

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about taking measurements directly from the body and ready garments.

## Slide 5: INTRODUCTION
Sizing quality refers to the dimensional accuracy of the finished garment.
Measurements is an important step for drafting basic bodice block.

## Slide 6: BODY MEASUREMENTS AND THEIR IMPORTANCE
Fit is the most important factor leading to the final acceptance or refusal of any garment.
To achieve the best fit of the garment it is important to take body measurement accurately.
Therefore, standard measurement sizes are created and made available for commercial pattern.

## Slide 7: PREPARATION FOR MEASURING
For taking measurements following points must be considered:
A superior quality measuring tape should be used.
The metal end of the tape should to be used for vertical measurements and the other end for horizontal & circumference measurements.
The measurements should be taken over a smooth fitting foundation garment and never over bulky garments.

## Slide 8
Comfortable measurements should be taken rather tight or loose ones.
Hold the tape parallel to the floor for horizontal measurements, & perpendicular to the floor for vertical measurements.
While taking measurements one should record them in the books.
maybe this needs to be in bullets for better understanding.

## Slide 9: PRECAUTIONS WHILE RECORDING MEASUREMENTS:
While recording measurements a tailor must make sure the person whose measurements are to be taken is standing straight up right and not slouching.
For taking round measurements he must make ensure that the measuring tape snugs the body and there is no slack.

## Slide 10
He must also make the customer feel comfortable while giving his/her measurements.
He must know when to take straight measurements and when to take circumference measurements.
Circumference measurements are to be taken from the fullest parts.
The measurements must immediately written on paper so that the chances of forgetting them decreases.

## Slide 11: MEASUREMENTS NEEDED FOR THE CONSTRUCTION OF GARMENTS
Body measurements are taken according to the requirements based on the desired fit and style of the garment.

## Slide 12: Measurements for children’s garments
S.No. | Measurements needed
1 | Round chest
2 | Round waist
3 | Round hip
4 | Round neck
5 | Across shoulder
6 | Back and front waist length

## Slide 13
7 | Armscye depth
8 | Short or full sleeve length
9 | Sleeve circumference
10 | Waist to ankle
11 | Round knee
12 | Inseam
13 | Shirt length
14 | Pants or shorts length
15 | Crotch length
16 | Crotch depth
17 | Frock or skirt length

## Slide 14: Measurements Needed for the Construction of Garments for males
S.No. | Measurements needed
1 | Round chest
2 | Round waist
3 | Round hip (seat)
4 | Round neck
5 | Across shoulder
6 | Back and front waist length

## Slide 15
7 | Short or full sleeve length
8 | Armscye depth
9 | Round cuff
10 | Waist to ankle
11 | Round upper arm
12 | Inseam
14 | Crotch length
15 | Crotch depth
16 | Pant length
17 | Shirt length

## Slide 16: Measurements Needed for the Construction of Garments for females
S.No | Measurements needed
1 | Round bust
2 | Round waist
3 | Round hip
4 | Across shoulder
5 | Round neck
6 | Armscye depth
7 | Upper arm circumference
8 | Lower arm circumference
9 | Elbow circumference
10 | Round knee

## Slide 17
12 | Back and front waist length
13 | Shoulder to bust
14 & 15 | Sleeve length (full/half)
16 | Waist to hip
17 | Waist to ankle
18 | Round thigh
19 | Round calf
20 | Round ankle
21 | Inseam

## Slide 18
22 | Skirt length
23 | Body rise (crotch length)
24 | Crotch depth
25 | Distance between bust points

## Slide 19: METHOD AND SEQUENCE OF TAKING BODY MEASUREMENTS
1. Female body measurements
Bust | A
Waist | B
Hips | C
Back width | D
Front chest | E
Shoulder | F
Neck size | G
Sleeve | H

## Slide 20
Under bust | J
Wrist | N
Upper arm | O
Calf | P
Ankle | R
Nape to waist | G-B
Waist to hip | B-C
Front shoulder to waist | F-B

## Slide 21: BODICE MEASUREMENTS
Bust: Measure around the fullest part of the bust placing the tape just below the shoulder blades at back.
Waist: To be measured around the waist where the pants or bottoms to be worn.
Hips: To be measured around the fullest part of the hip.
Back width: To be measured across from center of armscye to armscye on back side.

## Slide 22
Front Chest: To be measured across from center of armcye to armscye.
Shoulder: Measure from the neck joint to the arm joint along the middle of the shoulder.
Neck: To be measured at the round of neck at just above the collar bone in the front.
Sleeve: To be measured with arm bent from highest point of shoulder to wrist.
Under the Bust: To be measured around under the bust.

## Slide 23
Wrist: To be measured around (Fig.4.1aN).
Upper arm: To be measured around the upper arm.
Calf: To be measured around the calf just below the knee.
Ankle: To be measured around the narrowest part of ankle.
Nape to waist: To be measured from nape of neck from to waistline passing through the center of the bust.

## Slide 24
Front waist length: To be measured from edge of neck from shoulder to waistline passing through the fullest point of the bust.
Shoulder to bust: Measure down from highest point of shoulder to tip of bust.
Distance between bust points: Measure in the horizontal direction, the distance between the two bust points.
Back width or across back measurement: Measure across the back from armhole to armhole about 3 inches below base of neck on line A.

## Slide 25
Back waist length: To be measured from the centre point of back neck to the centre point of waistline.
Armscye depth: Measure from base of neck at centre back to a point directly below it an in level with the bottom of the arm where it joins the body.
Upper arm circumference: To be measured from the fullest part of the arm.
Lower arm: Measure around the arm at desired level corresponding to lower edge of sleeve.

## Slide 26
Elbow circumference: Measure around the arm elbow (at H in Fig.4.4a).
Wrist: Measure around the wrist (N in Fig.4.4a)

## Slide 27: 2. Skirt Measurements
Waist: To be measured around the waist where the pants or bottoms to be worn.
Hip: To be measured to the fullest part of hip in round. (This level will be about 7 to 9 inches below the waist for an average figure).
Waist to hip: Measure down from waist at centre back to fullest part of the hip.
Skirt length: As per requirement the length is to be measured from waistline to the desired length.

## Slide 28: 3. Leg Measurements
Round thigh: It is measured around the thigh.
Round knee: To be measured by keeping the measuring tape on the round knee and then folding the leg (calf touches the thigh) to get the correct measurement.
Round calf: It is measured around the fullest part of calf.
Round ankle: It is measured around the ankle.
Inseam: Measure down the inner leg seam from crotch to the bottom of the leg.

## Slide 29
Body rise: Measure at the side seam from the waistline to the base of a chair/flat surface when seated.
Leg Length: Measure at the side from waist to the foot.

## Slide 30: 4. MALE BODY MEASUREMENTS
Shirt Length: Shirt length should be measured from base of the neck to desired length.
Pant Length: Pant length is measured from waist to ankle along with side of the body.
Round Cuff Measurement: Cuff measurement is estimated by measuring the wrist loosely and adding ½” overlap extension to it.

## Slide 31
The measuring tape should be handled with neither pulling a tape nor to loose while taking measurements.
Measurements to be taken in a sequence for customer convenience.
All girth measures should be taken with 2 fingers inside the tape-neither tight nor loose, to give the ease for movement
To avoid any mistake, the measurements should be taken twice.

## Slide 32: PRECAUTIONS WHILE TAKING BODY MEASUREMENTS
An initial communication regarding the design, cuts, style, and specific requirements (buttons, collar, pockets, seams).
Careful and silent observation on customer style, fit or other deviation in figure proportion to be observed and to be noted in diary.
One must stand erect in front of the mirror while measurements are to be taken.

## Slide 33: Summary
In this session you have learnt about taking measurements directly from the body and ready garments.

## Slide 34: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma