## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 1: INTRODUCTION TO CLOTHING, TAILORING AND SEWING MACHINE
Session 1: Sewing Machine And Its Types

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Evolution of clothing | 5
Self employed tailor | 6
Sewing machine and its types | 7
Types of feed mechanism | 19
Summary | 25

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about evolution of clothing and types of sewing machines.
Explain about types of feed mechanism.

## Slide 5: INTRODUCTION – EVOLUSION OF CLOTHING
Pre-historic or cave men stringed the leaves in row and wore them as garments to cover themselves which became the first form of adornment.
Later fabrics such as cotton, wool, jute etc., were joined together by hand using needles made of bones and threads drawn from plant fibers.

## Slide 6: SELF-EMPLOYED TAILORS
Tailor is a person who stitches garment according to need and style of the particular customer at a reasonable price.
It is a small venture but requires high skill and knowledge.
A tailor’s major work involves styling, cutting, sewing and mending clothes.

## Slide 7: SEWING MACHINE & ITS TYPES
The following are the main categories of sewing machine based on their use:
Domestic Sewing Machine
Industrial Sewing Machine

## Slide 8
1. DOMESTIC SEWING MACHINE
With little changes, these machines can perform a variety of stitch types.
These are used by people for dressmaking, and home furnishing items.
These are usually used in homes by people simply interested in sewing.
Domestic sewing machines usually work on lightweight fabrics or work pieces.
These machines run on significantly smaller motors compared to that of the industrial sewing machines.

## Slide 9
2. INDUSTRIAL SEWING MACHINES
Industrial sewing machines are a heavy-duty version of a standard basic sewing machine, and it is used for mass production.
An industrial machine is well equipped with a clutch and large servomotor and can sew thousand stitches per minute.
These are used to sew heavier material like leather, canvas, vinyl etc.
Some programmable machines can store 10–30 or more patterns in the memory.

## Slide 10: CLASSIFICATION OF SEWING MACHINE BASED ON MACHINE TYPE
Mechanical Sewing Machines
Electronic Sewing Machines
Computerized Sewing Machines

## Slide 11: 1. MECHANICAL SEWING MACHINES
These machines are less expensive and are the simplest type of sewing machines in terms of build.
They are classified as follows:
Hand-operated Sewing Machine
Treadle Sewing Machine

## Slide 12
i. HAND-OPERATED SEWING MACHINE
This is the simplest form of domestic sewing machine which is operated by hand.
A handle is attached to the fly wheel which is detachable and is used to operate the machine.
A hand-operated sewing machine is generally used for domestic purpose and for simple projects.
This machine is suitable where there is no electricity supply.

## Slide 13
ii. TREADLE SEWING MACHINE
This machine is operated by feet, with an additional peddle attached to the machine.
A belt is attached to the lower peddle passing through the balance wheel and is driven by feet.
These machines run faster than the hand-operated sewing machine.
This machine is also suitable for the places where there is no electric supply.
When handling the treadle sewing machine, both the hands of the Operator are free to handle the fabric.

## Slide 14: 2. ELECTRONIC SEWING MACHINE
Operated with the help of electric motor this machine reduces the efforts of moving the treadle or hand operation.
In the electronic machines, balance wheel comes to motion by a belt, which is attached to an electric motor.
A single motor supplies power to the needle.
It is essential to control the speed of this machine by putting pressure on an electronic foot pedal.
Practice is essential to handle an electric sewing machine.

## Slide 15: 3. COMPUTERIZED SEWING MACHINES
They are computer operated and do not require any manual effort for their operations.
These sewing machines are very fast and specific to use.
A computerized sewing machine works with the help of various software.
Computerized sewing machines allow the tailor to adjust the functions according to the sewing needs.
These advanced computerized machines have an LED/LCD display or touch screen that helps to feed & change instructions.

## Slide 16: CLASSIFICATION OF SEWING MACHINE ON THE BASIS OF MACHINE BED AND FEED MECHANISM
Flatbed - This machines has arm and needle extend to the flat base of the machine used for sewing flat pieces of fabric together.

## Slide 17
Cylinder bed - These machines have a narrow, horizontal column which allows fabric to pass around and under the column. It allows easy rotation of tubular or cylindrical pieces such as cuffs.
Post bed - These machines include bobbins, feed dogs in a vertical column that rises above the flat base of the machine.

## Slide 18
Feed of the arm - Material is fed along the axis of a horizontal column. The design limits the length of the seam sewn to the length of the column.

## Slide 19: TYPES OF FEED MECHANISMS
The main types of feed mechanisms are as follows:
Drop feed: The feed mechanism lies below the machine's sewing surface. The fabric moves with every stitch by the movement created by feed dog.

## Slide 20
Needle feed: The needle itself acts as the feed mechanism, which minimizes slippage and allows tailor to sew multiple layers of fabric.
Differential feed: In such mechanism a set of two individual feed dogs are responsible for moving the fabric.

## Slide 21
Top feed: In such feed mechanism two sections of presser foot are used. One section holds the fabric while the other moves the top fabric layer.
Unison feed: It is a combination of needle feed and top feed where both needle and a two-section presser foot are responsible for the feed.

## Slide 22
Puller feed: In this system a roller is used along with drop feed mechanism to pull the fabric after each stitch.

## Slide 23: OTHER SPECIALIZED SEWING MACHINES
Lock stitch machine
Chain stitch machine
Double chain stitch machine
Buttonhole machine

## Slide 24
Button stitch machine
Bar-tack machine
Over-lock machine
Blind stitch machine
Over-edge machine

## Slide 25: Summary
In this session you have learnt about evolution of clothing, different types of sewing machine, different types of feed mechanism and other specialized sewing machine.

## Slide 26: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma