## Slide 1: JOB ROLE – SELF EMPLOYEED TAILOR
Class XI
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 1947)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 2: SEWING TOOLS & SEWING MACHINE OPERATIONS
Session 1: Measuring & Marking Tools & Their Usage

## Slide 3: Content
Title | Slide No.
Session Objectives | 4
Introduction to various marking tools | 5
Summary | 13

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about equipment used for measuring, and drafting.

## Slide 5: SELECTION OF TOOLS AND EQUIPMENTS
The process of garment construction includes the knowledge and skills of measuring, marking, cutting and stitching, which is done using appropriate tools.
Different tools and equipment of measuring, marking and cutting have their own utility and importance that makes the work easier and quicker.

## Slide 6
TOOLS AND EQUIPMENTS
1.Measuring tools:
Measuring tools are essential for accurate measurements which ensure a perfect fit and fall in a garment. Types of measuring tools:
Tape measure: It is a 60 inch (150 cms) long flexible tape with markings on both sides and metal tipped ends used for taking body measurements.

## Slide 7
Yardstick/Metric rule: It is a metre scale made of hardwood or metal used to draw long seam lines on paper or fabric.
Ruler: A ruler measuring 6, 12 or 18 inches is used for measuring and drawing small straight lines while drafting patterns and cutting.
L-square or tailor’s square: It is a 24 x 14 inch L-shaped ruler with two arms forming a 90º angle.

## Slide 8
Sewing gauge: It is a small 6-inch (15 cms) plastic or metal ruler with a slider used for marking short lengths like hems, buttonholes, etc.
French curve: It is made of plastic, wood or metal templates with an edge composed of varying radii/curves used for shaping the armhole and neckline.
Vary form curve: It looks like elongated French curve and is used for blending and shaping curves of collar design, sleeve caps, etc.

## Slide 9
Following are the marking :
Tracing wheel: Tracing wheels are of two types:
Serrated edge wheel: They make a dotted line while transferring markings.
Smooth edge wheel: They produces a solid line and used for delicate fabrics like silk or chiffon.
2. Marking tools:

## Slide 10
Tracing papers and sheets: It is a waxed tracing paper used with the tracing wheel for transferring the markings.
Tailor’s chalk wedges: These are thin pieces of hard chalk available in several colours for marking construction lines and alteration marks while fitting.
Tailor’s wax: It has a consistency like that of a crayon and suitable for use on wool or worsted materials.

## Slide 11
Liquid marking pens: These can be used for marking if the marks disappear after 48 hours or wash off from the fabric.
Pins: Pins are used for holding the fabric layers together while cutting and sewing.

## Slide 12
Awl/stiletto: It is a pointed metal tool used for piercing holes in pattern.
Notcher: It is used to cut small opening/notch on pattern.

## Slide 13: Summary
In this session you have learnt about tools and equipment used for measuring and drafting.

## Slide 14: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma