## Slide 1: JOB ROLE – SEWING MACHINE OPERATOR
Class X
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 0301)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 3: FASTENERS IN GARMENTS
Session 2: Sewing Techniques Of Fasteners

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Sewing techniques of fasteners | 6
Summary | 12

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about sewing techniques of fasteners.

## Slide 5: BUTTON SEWING TECHNIQUE
Draw the thread through one hole of the wrong side of the button
Down through the opposite hole of the correct side of button into the fabric
Repeat the action 4-6 times
Wind the thread tightly
Knot and cut the thread

## Slide 6: SEWING SHANK BUTTON
Secure the thread and bring the needle to the surface.
Bring it through the hole in the shank.
Take the needle down through the fabric and back to the surface again.
Repeat, making several stitches through the shank and fabric.
Work on the wrong side to secure the thread.
Once the threads are secure, fasten off.

## Slide 7: BUTTONHOLES SEWING TECHNIQUE
Mark the position and side of each buttonholes
Work form right to left on the lower edge of the slash.
Using a short stitch, sew (1/8 inch) along each side of this horizontal line and across the other end of the buttonhole.
Slash carefully between the stitching with small sharp scissors.
Overcast the raw edges using a thread
Insert the needle in to the slash and bring it out at the line of tacking stitches below.
Loop the thread around the needle point from left to right.
When you get to the corner, fan the stitches and reinforce it.
Stitch along the length of the slash using this technique.

## Slide 8: HOOKS & CLASPA SEWING TECHNIQUE
Hold the hook firmly between the finger and thumb.
Work down toward the second position and close the rings.
Pass the needle up from the eye/ring between the fold to the second position
Pass the needle up between the fold and bring it out to the left
The stitches should not pass through the right side.
Sew three or four times over the shank.
Close under the nose and work three or four stitches.

## Slide 9: THREAD EYE SEWING TECHNIQUE
Mark the position of the eye.
Secure it from the wrong side of the fabric
Sew buttonhole stitches all along over these threads
Using double threaded needle make a stitch as wide as you to slip the hook onto it
Repeat this for 2-3 times to make the base strong
Stitches till the whole thread is covered in buttonhole stitches.

## Slide 10: PRESS STUDS SEWING TECHNIQUE
Mark the position for the stud taking care to match the lap of the opening.
Place the socket side of the press stud on the under-lap of the garment,
Sew through each hole several times, going under the press stud as we sew from hole to hole.
The stitches should not come on the right side of the garment.
Fasten the thread securely when the press stud is sewed.
Place the ball portion on the overlap
To sew on the socket, align the 2 part of the press studs by putting the needle through the centres of both studs.

## Slide 11: ZIPPER SEWING TECHNIQUE
Align the lower end of the zip so that it tucks into the hem.
Always try to pin from the bottom of the zip upwards.
Tack each side of the zip opening and then press the seam before putting in the zip. Fold the facing and hem down over the tapes.
To stitch the rest of the seam, first close the zip.
Finish off the seam in the appropriate way for the fabric.

## Slide 12: Summary
In this session you have learnt about sewing techniques of fasteners.

## Slide 13: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma