## Slide 1: JOB ROLE – SEWING MACHINE OPERATOR
Class X
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 0301)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 1: BASICS OF GARMENT CONSTRUCTION-II
Session 2: Stitching And Application Of Seams

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Seam type and their applications | 6
Summary | 22

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about different types of seams and their applications.

## Slide 5: SEAM
A seam is a technique of joining two or more pieces of fabric together by a row of stitches.

## Slide 6: APPLICATION OF SEAMS
The selection of correct seam is important before application of seam in a garment.
The type of seam to be used in a garment will depend on various factors.

## Slide 7: Factors affecting selection of seam
Texture of the fabric
Design of the garment
Place where seam in used
Current fashion

## Slide 8
Texture of the fabric: It is a determining factor, as the fabric and its firmness will decide the type of seam, which has to be applied. For example, when working with a heavy fabric, thick seam like French seam must be avoided.
Design of the garment: Seams may be straight or curved based upon the garment design. While joining curved edges, use of plain seam will give a better finish compared to any other type of seam. Parts of the garment that may get stretched during body movement should be made with seams that are more durable.

## Slide 9
Place where seam in used: The pressure that will be applied on the seam while wearing the garment determines its construction. For example, when making boys’ sports shorts, a strong seam like flat and fell seam should be used.
Current fashion: It is a major factor to be considered while selection of seams. Cuts of a garment are directly affected by the current fashion and so are the seams.

## Slide 10: TYPE OF SEAMS
Plain Seam: It is the most basic seam and joins two or more layers of fabric with a single line of stitching.
APPLICATION OF PLAIN SEAM
It is used on all types of fabrics except on very transparent fabrics.
It is suitable for firm fabrics that do not ravel.
It is used for fabrics that will not be subjected to hard laundering.
This is used for side seams, underarm seams and armhole seams.

## Slide 11: Construction of plain seam
Take 2 pieces of fabric of 25 X 10 cm
On wrong side mark a line 1 cm away from the edge lengthwise.
Pin both pieces with right side facing each other
Baste on the line by hand and remove the pins.
Position the needle on the seam line.
Stitch back to the end & then stitch forward on seam line.
Trim and remove the basting threads
Press the seam allowances open.

## Slide 12
Run and Fell Seam: This is a flat durable seam used on men’s sports shirts, work clothes and children’s clothes and pyjamas.
APPLICATION OF RUN AND FELL SEAM
It is used on men’s sports shirts, work clothes and children’s clothes and pyjamas, etc.
It is also used in the production of jeans because of its strong construction

## Slide 13: Construction of run & fell
Take 2 pieces of fabric of 25 X 10 cm
Pin the wrong sides together
Sew the fabric at 1cm away from the edge
Press the seam
Trim the seam allowance to reduce bulk
Enclose the top seam allowance under the bottom seam allowance.
Stitch along the folded edge

## Slide 14
Bound Seam: A variation of seam finishes, bound seam fastens the raw edge by using another strip of binding over it.
APPLICATION OF BOUND SEAM
Bound seam in especially good for finishing seams in an unlined jacket or coat.
It is also used in traditional men’s kurta.
It is not a good option in case of very bulky fabrics.

## Slide 15: Construction of bound seam
Press open a seam having 2 cm seam allowance.
Trim one seam allowance to 3 mm.
Turn the other seam allowance by 3 mm and press.
Turn and press again and bring the trimmed edge which is now enclosed.
Stitch close to the fold as near as possible to the first line of stitching.

## Slide 16
Lapped Seam: This seam is used for joining sections of interfacing two avoid bulking, that is a mass of fabric getting thick.
APPLICATION OF BOUND SEAM
It is a rarely used seam.
This seam is used for joining a gathered or unaltered section to a straight edge, as in a yoke.
Mainly used for seaming denim jackets, jeans and overalls.
Other application are: fabrics that will not ravel, unlined garments, side seams of shirts, etc.

## Slide 17: Construction of lapped seam
Mark a line 1 cm from each edge of two pieces of fabric.
Lap one edge of the sample piece over the other with lines meeting in the center of overlapping portion and baste it.
Place a row of straight stitches on either side of the mark.
Trim both seam allowances close to stitching.

## Slide 18
Counter Seam: Durable flat seam used for very thick materials, usually for men’s wear and reversible garments.
APPLICATION OF BOUND SEAM
It is used in thick garments to avoid bulkiness and secure raw edges as well.
It is the best seam to be applied on reversible garments, in which both the sides of the garment are meant to be a finished surface.
It is also used while applying borders to a garment.

## Slide 19: Construction of counter seam
On wrong side (WS) of one piece of fabric turn down a little, then turn on right side (RS) of the other piece and iron the firmly.
Place wrong side of the first piece of fabric on the right side of the second piece along the edges,
Machine stitch along the folded edge. This is termed as three-layered counter seam.

## Slide 20
French Seam: This is a ridge seam and is used on transparent and delicate fabrics, to give a neat look and durable finish.
APPLICATION OF BOUND SEAM
It is commonly used for rain wear.
It is suitable for edge stitching front facings on jackets and dresses.
It is applied on very transparent fabrics like net and chiffon, etc.

## Slide 21: Construction of French seam
placed 2 pieces of fabric together with wrong sides facing
Work a row of stitching 3mm
Press the seam and turn it
Crease the first row of stitching so that it is directly on the edge
Tack and stitch along the seam line about 3mm from the fold.

## Slide 22: Summary
In this session you have learnt about different types of seams and their applications.

## Slide 23: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support– Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma