## Slide 1: JOB ROLE – SEWING MACHINE OPERATOR
Class X
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 0301)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 1: BASICS OF GARMENT CONSTRUCTION-II
Session 1: Garment Construction Terminologies

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Terminologies | 6
Summary | 18

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about basics of garment construction and its terminologies.

## Slide 5: INTRODUCTION
Garment construction terminology refers to the various terms used while construction of garments.
This includes the terms used to define the various construction processes and the different components of a garment.

## Slide 6: TERMINOLOGIES
Basting needle
This is a sharp, long hand sewing needle which penetrates into fabric easily.
Bias binding/Bias tape
It is bias cut strip used for covering raw edges of neckline, armhole etc.
Bias draping
Designing of garment making pattern on a drape using bias grain fabric

## Slide 7
Bicep circumference
The measurement around the fullest part of the arm.
Blanket stitch
It is used for finishing a fabric edge.
Blocks/Sloper
A block pattern is a custom-fitted, basic pattern which can be altered to create designs for many different styles.

## Slide 8
Bodice
The front and back upper part of a pattern or garment that runs from shoulder to waist.
Buckram
A heavy, coarse stiff cotton fabric used for interfacing and stiffening parts of garments such as collars, cuff and hats.
Casing
This is a stitched cover of fabric which holds elastic, cording, or bonding.

## Slide 9
Chalk-trace
Pin through pattern markings, remove pattern leaving pins in place, and chalk mark the fabric using pins as a guide.
Collar stand
It is a band between the neckline and the collar on a shirt or a blouse.
Facing
It is an extra layer of fabric stitched on the inner side of a garment for strength and edge finishes.

## Slide 10
Fade-out pen
A fabric pen with ink that disappears 12 to 24 hours after marking.
Finger press
A method to temporarily flatten a seam using the heat from one’s fingers.
French curve
A drafting tool that enables one to draw smooth curves for e.g. armholes.

## Slide 11
Gore seams
Seams that hold gores together.
Hip curve
A curved ruler used to gives shaping on the pattern at hip area.
Invisible stitch
Small stitches made at a distance of 2mm or 3mm intervals at the side fold of the turn-under allowance to hold two pieces together.

## Slide 12
Invisible zippers
A zipper designed to disappear into a seam when sewn in.
Lapel
Part of collar that shows on the right side of garment.
Match point
A point marked on one pattern piece for matching a similar point marked on a second pattern piece.

## Slide 13
Multi size pattern
A commercial pattern printed with several sizes on each pattern piece.
Outline
The outline of a pattern is usually the cutting line.
Piping
A narrow piece of bias-cut fabric stitched over the raw edges of neckline and armhole to give a clean appearance to the garment.

## Slide 14
Placket
It is a opening/slits in upper and bottom wear for easy removing and wearing of the garment.
Quilt
Small pieces of fabric sewn together in layers and topstitched, for example coverlets or wall hanging
Rise
The distance between the waistband and the crotch seam on pants.

## Slide 15
Rolled hem
It is a very narrow hem created by rolling and stitching edge of fabric.
Ruching
Trimming created in a garment by pleats, flare or gathers.
Slash and spread
Cutting and spreading a section of pattern to add fullness.

## Slide 16
Sleeve board
Small ironing board that fits inside a sleeve.
Tapestry needle
A needle with a blunt tip and large oval-shaped eye made for decorative stitching with bulky threads or yarns.
Thread-trace
Transfer markings from the pattern to the fabric by hand basting stitches to duplicate pattern markings.

## Slide 17
Tulle
Fine net fabric commonly used for veils or gowns
Wash away stabilizer
It is type of support provided to a fabric which dissolves in water.

## Slide 18: Summary
In this session you have learnt about basics of garment construction and its terminologies.

## Slide 19: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support– Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma