## Slide 1: JOB ROLE – SEWING MACHINE OPERATOR
Class X
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 0301)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 2: STITCHING OF GARMENTS
Session 3: Assembling Parts Of Garment

## Slide 3: Content
Title | Slide no.
Session objectives | 4
Fabric marking and cutting of baby frock | 6
Summary | 12

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about assembling sequence of the garment.

## Slide 5: KEY POINTS FOR BETTER CONSTRUCTION AND STITCHING
The correct drafting of the garment
Layout of draft on cloth
Marking with stitch margins
Cutting done as per markings done
Stitching of garment components
Assembling parts of a garment
Finishing of a garment

## Slide 6: FABRIC MARKING OF BABY FROCK
Lay out the pieces along the grain.
Secure the pattern, with either weights or pins.
Using fabric marking tool trace around the pieces.
Mark all notches.
Now transfer darts and other details on the fabric by using carbon and tracing wheel or tailors chalk, etc.
Now the fabric is ready to cut.

## Slide 7: FABRIC CUTTING
Fabric cutting scissors can be used to cut out the pattern pieces.
One should keep in mind the alignment to avoid mistakes later on during sewing.

## Slide 8: GARMENT CONSTRUCTION FOR BABY FROCK
Cut both the frock panels along the outer line meant for cutting.
Attach placket at the back side of the frock.

## Slide 9: Neckline finish
The neckline can be finished with either facing or binding.
The facing is cut to the exact shape of the garment edge to which it is applied leaving 4cm all around and cut.
Place the facing for front and back neck respectively on the neck.
Make sure that the right sides of both the fabric are facing each other. Stitch the facing and frock panel together for front and back necklines.

## Slide 10
The armhole can be finished either with facing or binding.
Place both the bodice (right sides facing) and complete by a side seam

## Slide 11: Skirt finishing
Stitch the two skirt piece together along the sides after forming gathers.
Complete skirt by placing together the upper body and lower skirt and stitch them together.
Then the frock should be finished.

## Slide 12: Summary
In this session you have learnt about assembling sequence of the garment.

## Slide 13: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma