## Slide 1: JOB ROLE – SEWING MACHINE OPERATOR
Class X
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 0301)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 5: JOB CARDS IN GARMENT INDUSTRY
Session 3: Reporting Of Damage Or Fault In The Material

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Damage or faults in material | 5
Reporting the damage or faults in the material | 11
Summary | 12

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about identifying damage or fault in the material and reporting them.

## Slide 5: DAMAGE OR FAULT IN THE MATERIAL
Fabric faults can lead to wastage of both raw material and money.
Therefore to work effectively and efficiently the garment industry pays great attention to the quality of raw material and finished product.

## Slide 6: TYPES OF FAULTS
Bad Selvedge: A bad selvedge is the result of-
Loose or tight selvedge yarn in the Beam.
If the pick yarn is entangled into the shuttle box the bad selvedge is occurred.
If lower strengths yarn exist in the selvedge and comparatively fewer yarn can cause a bad selvedge of a fabric.
Unparalleled weaving shed causes the bad selvedge.

## Slide 7
Burl Mark: When a slub or extra piece of yarn is woven into the fabric, it is often removed by a burling tool creating a blur mark.
Drawbacks: It is caused by excessive loom tension gradually applied by some abnormal restriction.
Dropped Pick: It is caused by the filling insertion mechanism on a shuttle-less loom not holding the filling yarn, causing the filling yarn to be woven without tension. The filling yarn appears as "kinky” (i.e. loose).

## Slide 8
End Out: It is caused by yarn breaking and loom continuing to run with missing end.
Jerk-in: It appears on selvedge and is caused by an extra piece of filling yarn being jerked to part way into the fabric by the shuttle.
Knots: It is caused by tying spools of yarn together.
Mixed End (Yarn): Yarn of a different fibre blend used on the wrap frame, resulting in a streak in the fabric.

## Slide 9
Mixed Filling: It is a shade change caused by bobbin of lightweight yarn or different fibre blend used in filling.
Open Reed: It results from a bent reed wire causing wrap ends to be held apart, exposing the filling yarn.
Slub: It is usually caused by an extra piece of yarn that is woven into fabric.
Smash: It is caused by a number of ruptured wrap ends that have been repaired.

## Slide 10
Soiled Filling or End: Dirty, oil looking spots on the wrap or filling yarns, or on package-dyed yarn.
Stop Mark: When the loom is stopped, the yarn elongates under tension; when loom starts again' the slackness is woven into the fabric creating stop mark.
Thin Place: It is often caused by the filling yarn breaking and the loom continuing to run until the operator notices the problem.
Oil spot or stain: Discolouration on a local area in a fabric that may be resistant to remove by laundering or dry cleaning.

## Slide 11: REPORT ANY DAMAGE OR FAULT IN MATERIAL
He/she is supposed to give immediate verbal information to the Line In-charge/Line Quality controller/Mechanic.
Define the problem correctly.
Mention machine type and number.
The exact time of problem when it happened.
Precautionary action taken by him/her.

## Slide 12: Summary
In this session you have learnt about identifying damage or fault in the material and reporting them.

## Slide 13: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support – Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma