## Slide 1: JOB ROLE – SEWING MACHINE OPERATOR
Class X
Sector – Apparel, Made-Ups and Home Furnishing (Qualification Pack Code: AMH/Q 0301)
PSS Central Institute of Vocational Education Shyamla Hills, Bhopal – 462 013 , Madhya Pradesh, India
_________________________________________________
www.psscive.ac.in
1

## Slide 2
UNIT 2: STITCHING OF GARMENTS
Session 1: Garment Components

## Slide 3: Content
Title | Slide No.
Session objectives | 4
Garment components | 6
Necklines | 8
Sleeves | 10
Collars | 16
Yoke | 21
Cuff | 24
Summary | 35

## Slide 4: Session Objectives
The students will be able to:
Gain knowledge about different garment components such as neckline, collar, sleeves, yokes and cuffs.

## Slide 5: GARMENT COMPONENTS
A Garment is complete when its different parts are sewn together.
These different garment parts are known as garment components.
For example: the garment components are front, back, neckline, sleeves, collar, yoke, cuffs, placket and pocket.

## Slide 6: FRONT
It is section that covers the front body.
Its shape depends on our measurement and garment design.
It has front neckline and front armhole cut as per the shape.
DIFFERENT GARMENT COMPONENTS

## Slide 7: 2. BACK
It is section that covers the back body.
Its shape depends on our measurement and garment design.
It has back neckline and back armhole cut as per the shape.

## Slide 8: 3. NECKLINES
Neck is an important part of the garment as it allows the head to slip into the garment.
Necks are finished mainly as two ways:
Pinning piping and
Turning in the bias band

## Slide 9: Types of neckline
Round neckline
U-Shape neckline
Boat neckline
Square neckline
Glass neckline
V-Shape neckline

## Slide 10: 4. SLEEVES
It is the part of a garment which covers the arm at different levels.
The sleeve joins the garment in an armhole that encircles the arm over the shoulder.
Sleeve length varies from barely over the shoulder (cap sleeve) to floor-length.

## Slide 11: Types of sleeves
Set-in-sleeves: These sleeves are sewn to set into the basic bodice armhole. Types of sleeves are:
Puff sleeve: They are gathered at shoulders and caught in at the cuff to create puffy effect.
Petal sleeve: This sleeve is joined at the top two edges overlapping and no underarm seam

## Slide 12
Bell sleeve: The Sleeve has a full flare at the hem giving it a bell shape.
Cap sleeve: They are very short sleeves which only covers the upper part of the arm.
Bishop sleeve: The basic bishop sleeve is a long sleeve with lower fullness gathered controlled with cuff.

## Slide 13
Leg-o-mutton sleeve: This is a full gathered sleeve head which tapers to fit towards the wrist giving it the appearance of a leg of mutton.
Cowl sleeve: The cowl sleeve has extra cap height and width that is created by triangular additions and is cut on the bias grain of the fabric.

## Slide 14
Sleeve bodice combination: Patterns may be developed with the sleeve and the bodice attached, thereby eliminating the armhole seam. Types of sleeves are:
Raglan sleeve: It is joined to the bodice with a diagonal seam running from the underarm to the neckline.
Kimono sleeve: This is a long one piece sleeve that is an extension of the bodice and extends to the wrist.
Dolman/Magyar: In this sleeve there is one piece of bodice and sleeve with no armhole.

## Slide 15: Sleeve construction
Cut the cloth as bodice part & sleeve
Fold the hem of the sleeve
Stitch the hem of the sleeve
Sleeve hem is finished and is ready to attach to the bodice
Stitch the side seam and see the finished sleeve
Attach the sleeve to the armhole and stitch

## Slide 16: 5. COLLARS
In garment, a collar fastens around the neck and enhance the appearance of a garment.
It works both functional and decorative purposes.

## Slide 17: Types of collars
Flat collars: It is a one-piece collar that lies flat and close to the garment along the neckline, rising only slightly above the garment’s neck edge.
Peter pan collar: It is a round flat collar (one piece or two pieces) that sits flat and has rounded front collar edge.
Sailor collar: It has a wide band at the back that is tailored down to a deep ‘V’ neck at the front. It is a design feature of traditional sailors uniform.

## Slide 18
Standing collars: This is a close fitting collar which stands up stiffly against the neck.
Mandarin Collar: It is slightly more shaped and fits closer to the neck; it is also called Military, Nehru Jacket and Chinese collar.
Stand Collar: A standing collar is a band which stands up over the neck seam line.
Polo collar: It is close fitted, round and high collar that folds over and covers the neck. It is always cut on bias.

## Slide 19
Rolled collars: They are differentiated from flat collar by a roll line that breaks the collar into stand and fall areas.
Shirt collar: The shirt collar with band is composed of two separate pattern pieces, the band and a collar section.
Shawl collar: The shawl collar is a design in which the collar is cut as an extension of front bodice and then stitch together at center back.

## Slide 20: Collar construction
Iron the collar fusing by keeping it on the collar fabric.
Give edge stitch to the fusing with the fabric.
Insert the thread into the fabric on collar point and stitch for the sharp edge.
Trim the extra fabric.
Pull the thread from the fabric & Smooth the material
Give 1/4" Stitch or edges stitch of the fabric.
Give 1/4" Stitch on piece of a collar.
Keep a fabric on the finished collar piece.
Stitch both the collar pieces together.
Trim the extra fabric.
Iron & finish the collar.

## Slide 21: 6. YOKE
A yoke is a shaping device that provides support to the garment.
It is placed around the neck and shoulders, or around the hips/waist.

## Slide 22: Types of yokes
Round Yoke: It is a round shape yoke. Mostly used on baby’s frocks.
Straight yoke: It is mostly used in men’s shirt or back part of shirt.
Square yoke: This yoke is square in shape mostly used in women’s shirt in front side.
V’ Shape yoke: This yoke is mostly used at waistline.

## Slide 23: Stitching technique of a yoke
Cut two identical pieces of yokes
Stitching the inside yoke piece to the back of the shirt.
Attach the outer yoke piece with the right sides of the yoke facing shirt back
Press both yokes up
Cut the yoke seam allowance and press seam towards yoke.
Fold under the seam allowance of the inside yoke and press.
Topstitch along the yoke seam line
Stitch the center front pieces to the outer yoke with right sides.
Stitch the two layers of the yoke together in the seam allowance

## Slide 24: 7. CUFF
A cuff is an extra layer of fabric at the lower edge of the sleeve of a garment covering the arm, at the wrist.

## Slide 25: Types of cuffs
1. Barrel cuff: It’s have simple button closure. Types of barrel cuffs are:
One button barrel cuff: More subtle and shorter in length.
Long one button barrel cuff: More formal and longer in length.

## Slide 26
2. Rounded cuff: It is used for formal wear.
3. Mitered cuff:
One button mitered cuff: The one button mitered cuff is a dressy cuff. It has elegant mitered angled at the button closure.
Two button mitered cuff: The two-button mitered cuff is a popular dress shirt cuff.

## Slide 27
4. French cuff: It is a square cuff shape. The cufflinks is worn with it.

## Slide 28: Cuff construction
Cut 2 pieces for sleeves and cuffs
Cut a slit on both pattern piece opposite the front
Put the pattern piece and interfacing together
Stitch the top edge of the cuff with a half inch seam allowance
Cut right on the top of the slit and on the corners
Turn the cuff right sides out and iron it
To lock or close put the right sides together and sew along the sides
Sew the sides of the cuff right on the seam allowance
After sewing, iron the cuff
Turn the right sides out
Put a slit on the end of the pattern piece and interfacing

## Slide 29: 8. POCKET
A pocket is a piece of fabric attached on the outside or inside of a garment.
They are used to carry small articles, such as handkerchiefs or coins.

## Slide 30: Types of pocket
Patch pocket: patch pockets are applied on the outside the garment and can be functional and decorative.
In-seam pockets: the in-seam pocket is stitched neatly into the side seam of a garment.
Hip pockets: the hip pocket is the curved pocket design on the back side of the pants, trousers and skirts.
Inside set-in pocket/slash pocket: It is stitched into a cut opening made with a single or double welt, with or without a pocket flap.

## Slide 31: Construction of a patch pocket
Cut a piece of fabric for pocket
Fold 1” pocket piece
Iron the pocket piece
Attach the pocket piece to the bodice part & give edge stitch.
Finished pocket

## Slide 32: 9. PLACKET
Plackets are an opening in upper or lower part of the garment, mostly at the neck, waist of skirt, pair of a trouser and cuff of sleeve.
They are used for easy wearing or removing garment.

## Slide 33: Types of plackets
French placket
Concealed placket
Classic front placket
Bound placket
Partial button placket

## Slide 34: 10. BELTS
Belts can add a professional finished look to many garments, so select belts with care.
Belts are more of an accessory than a garment component.
There are various types of readymade belts available in the market, but costume made belts, according to the garment enhance the aesthetics of the garment.

## Slide 35: Summary
In this session you have learnt about different garment components.

## Slide 36: Project Coordinator : Prof. Pinki Khanna
Joint Director
PSS Central Institute of Vocational Education
Shyamla Hills, Bhopal – 462013 , Madhya Pradesh, India
______ _ _
E-mail: jdpsscive@gmail.com
Tel. +91 755 2660691, 2704100, 2660391, 2660564
Fax +91 755 2660481
Website: www.psscive.ac.in
© PSS Central Institute of Vocational Education, Bhopal 2020
Academic Support– Shivangi Vig & Nupur Srivastava
Assistance Graphic Artist
Vani Pandya Prachi Verma